Language for Analog Computing Engines (LACE)
# Version History
‍2025-12-31	document re-structured, consistent syntax	Dietmar Hiller
2025-09-11	general improvements	Dietmar Hiller
‍2025-08-14	weight in reserved words, examples	Dietmar Hiller
‍2024-10-07	define: some items are optional	Dietmar Hiller
‍2024-09-09	major rework of the syntax	Dietmar Hiller
‍2024-07-24	added division, assign	Dietmar Hiller
‍2024-07-05	renamed to LACE; removed brackets for some operations; parameters are separated by space, comma or line break	Dietmar Hiller
2024-06-01	added operation output, division in isum	Dietmar Hiller
2024-05-29	First draft, still work in progress	Dietmar Hiller

License: CC BY-NC-SA 4.0 (https://creativecommons.org/licenses/by-nc-sa/4.0/ )
# Abstract
The zenith of analog computers was reached in the 1960s. They were subsequently superseded by digital computers due to rapid advancements in the semiconductor technology.
In recent times, there has been a resurgence of interest in these devices for specialized applications, such as high-performance computing and artificial intelligence training because of their high speed and low power consumption.
Moreover, within scientific contexts, they provide a lucid approach for visualizing the effects of differential equation parameters, such as for harmonic oscillations, radioactive decay, gravity, and heat dissipation. This feature positions them as an invaluable educational resource, facilitating students' comprehension of the underlying physics principles. The employment of analog computers offers a distinct advantage, in that only the problem needs to be delineated. This stands in contrast to digital computers, where the solution must be programmed.
However, the configuration of such a computer is currently depicted with pictograms that correspond to symbols used in the electronics industry and are therefore not immediately comprehensible for a layperson.
LACE aligns with the natural language of mathematical processes and programming differential equations. The script can be formulated according to the differential equations, and subsequently the wiring on an analog computer following the script is performed. It also contains intrinsic documentation of the approach to solving the problem.
# Introduction
The basic concept of analogue computers has remained unchanged since the 1960s. They consist of discrete elements that perform calculations such as summing, integration, inversion and multiplication by a constant, as well as connections between these elements which define the flow of information [1].
This connection was performed in the 1960s manually with the use of patch cables. An approach that is still being used mostly at devices for educational purposes because of the simplicity of setting up a new algorithm [2][3].
Recent advancements in the field have focused on the development of a fully integrated device, incorporating calculation elements and a connection matrix on a single chip, serving as a technological foundation for low-precision, energy-efficient, and rapid computing [4]. However, achieving this final step is challenging due to the requirement for high linearity, low offset and low environmental dependency of the calculation elements.
As an intermediate step in the development of this technology, the elements are still realized by discrete components, with the connection being performed by an integrated connection matrix. This matrix can be configured by a standard digital computer. Additionally, the parameters, herein identified as coefficients, are managed through these digital computers on high-end devices [5]. Consequently, the device is often referred to as an analog engine, which is a component of a more extensive hybrid computer system.
# Basic Principle of Analog Computers
To demonstrate the fundamental concept of an analog computer, the solution of the differential equation of a damped harmonic oscillator is presented as an example.
The equation of motion for a viscously damped simple harmonic oscillator is governed by the differential equation m ddot{y} + D dot{y} + S y = 0 , with m the mass, D the damping proportional to its speed and S the spring constant. Initial conditions are the initial deflection y0 and the initial speed ẏ0 .
Analog computers are usually programmed using the Kelvin feedback technique [6][7] which requires the highest deviation on the left side of the equation: ddot{y} = -1/m (D dot y + S y) .
Traditionally, the programming of the engine is described with a patching diagram:

Understanding these diagrams requires some basic knowledge of electronics circuits. Further effort is required to document the steps for solving the problem. In an analogue computer, which allows the switching matrix for the wiring elements to be configured automatically, this diagram must be manually translated into the corresponding programming language.
LACE follows the sequence depicted above and uses semantics similar to those of general-purpose programming languages. Details will be explained in the syntax section below.
First the constants are assigned to coefficients:
coefficient.1(-1) -> y0’ # Initial speed
coefficient.2(-1) -> -y0 # Initial Amplitude
coefficient.3 -> S # SpringForce
coefficient.4 -> D # Damping linear to speed
coefficient.5 -> 1/m # 1/mass

Next carry out the integrations, taking into account the initial conditions:
iintegrate y'' -> -y'
  IC: y0’
iintegrate -y' -> y
  IC: -y0

Inverting -y’, multiplication by the constants and summing up:
invert -y' -> y'
cmultiply y, S -> S*y
cmultiply y',D -> D*y'
isum S*y, D*y' -> -(S*y+D*y')

Multiplication by 1/m and assigning the result to y’’, thus closing the Kelvin loop
cmultiply -(S*y+D*y'), 1/m -> -1/m*(S*y+D*y')
assign -1/m*(S*y+D*y') -> y''

To visualize the behavior for instance with an oscilloscope, the resulting value of y is coupled to an output.
output y -> out.y
# Basics
This chapter describes the basics of the language.
## Functions
The general syntax of functions is as follows:
function-name ([parameter_type:] parameter, ...) -> result
[parameter_type: parameter]
[parameter_type: parameter]

The brackets “()” and the comma are optional.
The parameter_type may be omitted if the allocation is unambiguous.
Parameters can be listed after the function name or separated in indented lines below. The later is recommended in order to improve readability.
The result of the function is written after “->”.
## Variables
Variable names can be chosen relatively freely. Thus, it is recommended to use readable formulas such as “A+B”. Only the reserved words are not permitted.
Variables with the same name are connected on the wiring board.
Keywords and variables are case sensitive.
### Reserved Words
The following expressions may not be used for variables. They may not
… contain
- <space>, <comma>
- :, #, ->
… be
- -1, +1
- 1*:, 10*:, 100*:
- assign
- capacitor
- cmultiply
- coefficient
- compare
- define
- diode
- GND
- GT0
- idivide
- iintegrate
- include
- invert
- isum
- multiply
- output
- out.x, out.y, out.z, out.u
- zdiode
## Comments
A comment starts with the character “#” and can be placed in a separate line or at the end of a command. All characters starting with “#” until the end of line are not interpreted.
## Include
To include the code of an external file use
include <filename>
This can be used if non-standard compound functions or functions realized on special external boards are needed.
# Standard Functions
The following functions are available on most analog computers:
## Assign
Assigns one variable_1 to variable_2. Thus both variables are identical. This is useful for the Kelvin feedback to connect the output of the circuit to the input of the differential equation. On the wiring board, these two variables are connected.
assign (variable_1) -> variable_2
## Computation
### Summing
isum calculates the inverted sum of the weighted input values -sum from{i} weight_i * variable_i = result .
isum ([weight_i*:] variable_i, …) -> result
[FB: variable_FB]
[SJ: variable_SJ]

The “i” before the word “sum” is used to make clear that the result is inverted.
weight_i can be 1*:, 10*: etc. The value of the variable is multiplied by this weight.
weight_i can be omitted for 1*:.
SJ stands for summing junction. It is used for the implementation of compound functions.
FB goes to the feedback line. It is used for the implementation of compound functions, in particular to generate an Open Amplifier.
### Integration
This performs an inverted integration of the sum of weighted input values over time -int left( sum from{i} weight_i * variable_i right) dt = result .
The “i” before the word “integrate” is used to make clear that the result is inverted.
iintegrate ([weight_i*:] variable_i, …) -> result
[IC: variable_IC]
[SJ: variable_SJ]
weight_i can be 1*:, 10*:, 100*: etc. The value of the variable is multiplied by this weight.
weight_i can be omitted for 1*:.
IC is the initial condition. It has the same sign as the input. If omitted 0 is used.
SJ stands for summing junction. It is used for the implementation of compound functions.
### Multiplication
#### of two variables
calculates the product of variable_x with variable_y: left( variable_x * variable_y = result right) .
multiply ([x:] variable_x, [y:] variable_y) -> result
#### of a variable with a constant
cmultiply (variable, constantname) -> result
The constantname is defined via a coefficient.
### Inverting
inverts the sign of variable giving result: left( -variable = result right) .
invert (variable) -> result
### Comparing
If the sum of variable_A and variable_B is greater than zero, then variable_GT0 is available at result, otherwise variable_LT0 is available.
compare ([A:] variable_A, [B:] variable_B) -> result
[GT0: variable_GT0]
[LT0: variable_LT0]

If either is not given zero will be used.
## Input / Output
### Coefficients
Coefficients are constants which can be set by the operator. They are recognized by an identifier (usually a number), which is provided after the word coefficient and a dot.
coefficient.<identifier> [(constant)] -> constantname

If the constant is given, which can be -1 or +1, the coefficient is generating a constant with name constantname which can be used e.g. as initial condition for integration. The constant is wired to the input of this coefficient.
Omitting the constant, the coefficient is used to cmultiply a variable with the value set by that coefficient.
It is advised to have all coefficients listed at the top of the code. This makes it easier to implement changes, for example if the identifier of the coefficients needs to be changed.
### Output
Describes variables which are connected to the output of the engine.
output(variable) -> <output_identifier>

<output_identifier> can be for instance (depending on the machine) out.x, out.y, out.z, out.u.
# Compound Functions
It may be necessary to use functions which are not readily implemented on the analog engine, but which can be set up using on- or off-board components.
In order to increase simplicity and readability, compound functions can be defined using the define function:
define function ([parameter type]: [variable-name] [, ...]) -> result
<definition>

The definition is a series of LACE-commands. For examples see below.
If the new function is already either intrinsically or explicitly defined, any subsequent define replaces the previous definition.
## Components
Some components may be needed to assemble compound functions.
### Capacitors
Capacitors are available with different capacitances. It’s value is the identifier:
capacitor.capacitance (input) -> output
### Diodes
diodes
diode (port: input) -> output

Ports are:
    • AN: anode (+)
    • CAT: cathode (-)
### Zener-Diodes
Zener diodes
zdiode (port: input) -> output

Ports are:
    • AN: anode (+)
    • CAT: cathode (-)
## Open Amplifier
The open amplifier can be used to generate further functionality.
It is realized by connecting the FB-port of a summer to GND.
define openamp ([weight_i*:] variable_i, …) -> result
isum ([weight_i*:] variable_i, …, FB: GND) -> result
## Division
Divide variable_1 by variable_2 giving result: - frac {variable_1} {variable_2} = result . Note the inverted sign of the result due to the usage of an open amplifier.
A division is an inverted multiplication. Thus it is realized by placing a multiplier in the return path of an openamp.
define idivide ([X:] variable_1, [Y:] variable_2) -> result
openamp (variable_1, OA) -> result
multiply (result, variable_2) -> OA
## Root
The root (-x) can be calculated in a similar way as the division. Note: the input has to be negative.
define root ([X:] variable_x) -> result
   compare (variable_x) -> -xLimited
      LT0: -x
   openamp (-xLimited, OA) -> result
   multiply (result, result) -> OA

The compare makes sure that the input is never positive, because this puts the circuit into an error, which only can be reset by un- and re-plugging the inputs of the multiplier. This is also the case when the operation mode has changed, e.g. from OFF to REP.
# Extensions
Extensions are compound functions that add additional functionality.
## Building an additional integrator with Openamp
Additional integrators can be built with an openamp
define iintegrate.additional (variable) -> result
   openamp (variable, SJ: variable_cp) -> result
   capacitor.1nF (result) -> variable_cp

The 1 nF capacitor is used as an example. It has to be identical to that of the standard integrators.
## Integration limitation
Adding a limit to the integration, i.e. a value, the result may not exceed.
define iintegrate.lim ([weight_i*:] variable_i, …, IC: variable_IC,
 limit: GT0) -> result
   iintegrate ([weight_i*:] variable_i, …, SJ: variable_DA) -> result
   diode (CAT: result) -> variable_DA

limit limits the output result:
- GT0: limits to values > 0.
  - As soon as the cathode of the diode gets negative, the input of the integrator is short-circuited to the output and inhibits further integration.
  - There is a small slag, thus the output takes a tiny negative value.
## Divide sum by a value
This extension adds the possibility to divide the sum by a small integer -left( sum from{i} weight_i * variable_i right) * (1 / divisor)= result
define isum ([weight_i*:] variable_i, …, DIV: divisor) -> result
isum ([weight_i*:] variable_i, …,
     [weight_j*:] result, …
        ) -> result

divisor can be 2, 3, …. Each connection of the result to the input increases the divisor by the value of the corresponding weight_j.
There are further tricks to divide a sum by a constant.
# Conclusion
The scripting language LACE (Language for Analogue Computing Engines) allows mathematical problems to be easily transcribed into code for analog computers. It is therefore ideally suited to educational purposes, as well as to the implementation of integrated analogue computers and engines.
The script can be followed manually or by an interpreter or compiler to perform the wiring on the analogue computing engine, thus simplifying the transition towards fully integrated devices with applications in high-end technologies, such as modern engineering and artificial intelligence training.
# Appendix