Analog Engine
Example Applications
This document includes examples of applications realized with an analog engine. The scripting language used is described in the document “Analog Engine Scripting Language”.
Author: Dietmar Hiller
# Version History
2024-01-08	Seperated Helper Functions and Scaling to “Technical Topics” / Moved code to separate files AESL / Analytical solution of the damped harmonic oscillator / Scaling amplitude and time	Dietmar Hiller
2023-10-06	Adapt to updated syntax: OUT.U use of ALIAS / corrected usage of operation time: OP-TIME instead of SPEED	Dietmar Hiller
2023-10-04	Added damped harmonic oscillator	Dietmar Hiller
2023-09-24	First draft	Dietmar Hiller

# Radioactive Decay
N’ = -lambda * N
+1 -> InitialValue -> N0
N’, IC:N0 -> Integrator.1 -> -N
-N -> Decay -> -lambda*N=N’
-N -> Inverter.1 -> N
Set microphone loudness to center value, oscilloscope: 5 ms/div.
Full code see “Radioactive Decay.AESL”
# Damped Harmonic Oscillator
The equation of motion for a viscously damped simple harmonic oscillator is m ddot{y} + D dot{y} + S y = 0 , with m the mass, D the damping with speed and S the spring constant.
Rewritten to y’’=-1/m * (Dy’+Sy).
An initial condition is required; we put the deflection to y0 and the speed to y0’.
Full code see “Damped Harmonic Oscillator.AESL”
## Analytical Solution
[https://brilliant.org/wiki/damped-harmonic-oscillators/ ]
Solutions of the viscously damped simple harmonic oscillator should be oscillations within some form of damping envelope. Ansatz is an exponential damping envelope of an oscillation:
y(t) = Ae^{-g t} e^{iat} = Ae^{t (ai-g)} = Ae^{rt}
where A is some constant and (r = ai-g) will be found. g and a are place holders to show the damping (g) and oscillation (a). Plugging this ansatz into the equation of motion yields:
(mr^2 + D r + S)Ae^{rt} = 0 newline drarrow r^2 + frac{D}{m} r + frac{S}{m} = 0
which is a quadratic equation in r with solutions:
r = - {frac{D}{2m}} +-i cdot sqrt{ {frac{S}{m}} - frac{D^2}{4m^2} }
Note that there are two roots r to the quadratic corresponding to the two general solutions:
y(t) = a_1 e^{-frac{D}{2m} t} e^{ i sqrt{{frac{S}{m}} - frac{D^2}{4m^2} }t} + a_2 e^{-frac{D}{2m} t} e^{ -i sqrt{{frac{S}{m}} - frac{D^2}{4m^2} }t}.
These solutions in general describe oscillation at frequency %omega = sqrt{{frac{S}{m}} - frac{D^2}{4m^2} } within a decay envelope of time-dependent amplitude %alpha(t) = e^{-frac{D}{2m} t} .
Note, the frequency of the oscillations is only depending on the spring constant, damping and mass, whereas the damping also depends on the mass.
For the undamped case (D=0) this gives
alignl y(t) = a_1 e^{i %omega t} + a_2 e^{-i %omega t} newline alignl y(t) = a_1 cdot (cos (%omega t) + i sin (%omega t)) + a_2 cdot (cos (%omega t) - i sin (%omega t)) newline alignl y(t) = (a_1 + a_2) cdot cos(%omega t) + i (a_1 - a_2) sin (%omega t) newline alignc a_1 + a_2 = A newline alignc i(a_1 - a_2) = B newline alignl y(t) = A cos(%omega t) + B sin(%omega t) newline alignc y(t=0) = y_0 = A newline alignc dot y(t=0) = v_0 = B %omega newline alignl y(t) = y_0 cos(%omega t) + frac{v_0}{%omega} sin(%omega t)
This can also be written as
alignl y(t)=b cdot cos(%omega t - %varphi) newline alignc "because of" newline alignc y(t)=b cdot (cos(%omega t) cdot cos (%varphi) + sin(%omega t) cdot sin(%varphi) ) newline alignc y(t)=b cdot cos(%varphi) cdot cos(%omega t) + b cdot sin(%varphi) cdot sin(%omega t) newline alignc "with" newline alignc x_0 = b cdot cos(%varphi) newline alignc frac{v_0}{%omega} = b cdot sin(%varphi)

## Scaling
As an example, we may use the following data for the damped harmonic oscillator:
Initial Position	y0	1,5 m
Initial Speed	y0’	-0,15 m/s
Spring Force	S	2,5 N/m	kg/s²
Damping	D	0,3 N/(m/s)	kg/s
Mass	m	0,06 kg
	1/m	16,667 kg-1

Critical values are initial position (1,5 m) and 1/m (16,667 kg-1). Spring force could be coped with by using a gain 10 input.
Please see the table below while following the description of the following steps.
First we take care of y0. We replace the length measured in meter with 10¹ meter, thus we make use of deca-meter. y0 and y0’ have to be adapted. See columns “deca-m” below. Spring Force and Damping remain unchanged because in base units the length gets canceled out.
Next issue is that 1/m is well above 1. We are representing the weight by 10-2 kg, so 10¹ grams (deca-g). See columns “deca-g”. This also influences spring force and damping, which now exceed our target range.
Now, the second is replaced by 10-1 (deci-s) seconds resulting in the columns “deci-s”. Note that this also performs time-scaling, so that one time-unit of the analog engine now corresponds to one deci-second instead of one second before.
After the last scaling we have the issue that y0’ is very close to zero. There are more advanced scaling techniques which manage to optimize the value range of each operational amplifier. For instance the initial speed is converted to a value very close to zero, which is not the optimal.
The fully scaled program can be found at “Damped Harmonic Oscillator scaled.AESL”. Note that the gain 10 inputs are used for SUMMER.2 in order to achieve damping and spring constant values:

Obtained damped oscillation with parameters above
Adapted parameters: D=1,69, y0'=-0,187; calculated T=9,97 ms