Analog Engine Scripting Language (AESL)
# Version History
‍2024-01-16	Replaced OUT by OUTPUT	Dietmar Hiller
‍2024-01-07	Added TIMEBASE, removed SPEED	Dietmar Hiller
2023-10-06	OUT.X instead of OUT_X etc. added ALIAS, OP-TIME include full potential of Anabrid-THAT	Dietmar Hiller
2023-10-04	Minor changes	Dietmar Hiller
2023-09-24	First draft	Dietmar Hiller

# Introduction
This documents describes a scripting language for analog engines. The intention is to show a language that can be easily read by the human eye same as being easily interpreted by a hybrid controlling computer to set up, control and run an analogue engine.
The general structure is influenced by the programming language COBOL. Thus the entire program is divided in divisions.
# Structure
Note that any line may contain the character “#”. This indicates that the rest of the line is a comment and thus will not be interpreted.
## IDENTIFICATION DIVISION
The identification division has merely documentation purposes for the program name, version history and comments.
Syntax:
IDENTIFICATION DIVISION
PROGRAM-ID <program-name, text>
VERSION <text>
COMMENT <text>
## ENVIRONMENT DIVISION
The environment division describes the engine the script is developed for and / or the requirements to the engine, such as the number of integrators etc. The host computer can evaluate if the script can work on the available analog engine.
Syntax:
ENVIRONMENT DIVISION
ENGINE <name of analog computer, text>
REQUIRES <operator, text> <number>
available operators are listed below
TIMEBASE <text, e.g. 1ms>

Items ENGINE and REQUIRES are alternative. An internal table contains a list of REQUIRES per allowed ENGINE.
### OPERATORs
The operators are numbered by adding a “.” and then a number to the name of the operator. E.g.: INTEGRATOR.1
#### CAPACITOR
Capacitance my vary. E.g. on Aanbrid-THAT there are
- CAPACITOR.100pF
- CAPACITOR.100nF
#### COEFFICIENT
Their input goes to an adjustable element and the output is the product of this element with the input.
#### COMPARATOR
Comparators allow conditional switching. If A+B>0, then the input to “GT0” (greater than zero) is available at the output jack, otherwise the input to “LT0” (less than zero) is available.
Ports:
- A:
- B:
- GT0: This port is connected to OUT if A+B>0
- LT0: This port is connected to OUT if A+B<0
#### DIODE
#### INTEGRATOR
Integrators integrate the sum of their (weighted) input values over time.
Ports:
- 1: default, weights the input by a factor of 1
- 10: weights the input by a factor of 10
- IC (initial condition) allows the start value of an integration to be set.
Integrators change the sign of their output values implicitly.
#### INVERTER
Inverters yield the input value with the opposite sign.
#### MULTIPLIER
Multipliers multiply values supplied to their inputs.
Ports (both may be omitted):
- X
- Y
#### OPEN_AMP
Open Amplifier. This can be used to construct new functions, e.g. root (x), division etc. On Anabrid-THAT it can be realized by connecting port FB to GND in a SUMMER.
Ports:
- 1: default, weights the input by a factor of 1
- 10: weights the input by a factor of 10
#### SUMMER
Summer yields the negative sum of the weighted inputs.
Ports:
- 1: default, weights the input by a factor of 1
- 10: weights the input by a factor of 10
#### Z-DIODE
Zener-Diode
## DATA DIVISION
The data division describes input and output of data. Input is usually done by potentiometers that define constants for the equation and which can be set via an digital to analog converter in a hybrid solution. Output is the result of the calculation or any intermediate value.
Syntax:
DATA DIVISION
INPUT <input port, text> <variable name>
OUTPUT <output port, text> <variable name>
<output port>: OUTPUT.X, OUTPUT.Y, OUTPUT.Z, OUTPUT.U etc.
ALIAS <element> <alias>
- instead of using <element>, the <alias> may be used in the program
- e.g. ALIAS Coefficient.1 spring-constant

### Variable name
The name of a variable can contain any kind of characters. E.g. it is recommended to use readable formulas such as “A+B”. Only the reserved words are not permitted.
## PROGRAM DIVISION
The program division describes the “wiring”; the interconnection of the engine’s elements. The host computer interprets this part and sets up the logic of the analog engine.
Syntax:
PROGRAM DIVISION
<port:input> -> OPERATOR -> <output>
- <input> and <output> are variable names. Same variable names are connected.
- a port is a special connection of the OPERATOR (see below). It can be omitted for default ports.
- variable names can be set “equal” (e.g. y = y’’). This is useful to wire a Kelvin feedback
- multiple variables per input are separated by “,”
## OPERATION DIVISION
The operation division defines parameters of the operation. Examples are operating time settings, single or repetitive runs, halt conditions.
Syntax:
OPERATION DIVISION
MODE {REPEAT | SINGLE}
OP-TIME <operation time in s or ms>

HALT <condition>
condition can make use of any output variable, e.g. y<=0. Once the variable y is equal to or below zero, the operation is halted.
# Reserved Words
The following expressions may not be used as variables.
- #, ->
- -1, +1
- 1, 10
- ALIAS
- CAPACITOR
- COEFFICIENT
- COMMENT
- COMPARATOR
- DATA
- DIODE
- DIVISION
- ENGINE
- ENVIRONMENT
- IDENTIFICATION
- INPUT
- INTEGRATOR
- INVERTER
- MODE
- MULTIPLIER
- OP-TIME
- OPEN_AMP
- OPERATION
- OUTPUT
- PROGRAM
- PROGRAM-ID
- REPEAT
- SINGLE
- SUMMER
- TIMEBASE
- VERSION
- Z-DIODE