Description language for ANalog Circuit Engines (DANCE)
# Version History
2024-04-18	First draft, still work in progress	Dietmar Hiller

License: CC BY-NC-SA 4.0 (https://creativecommons.org/licenses/by-nc-sa/4.0/ )
# Introduction
DANCE is another scripting language for analog engines. In contrast to AESL, which is focused on connectivity of the engine, it is rather focused on user readability and simplicity. Thus realizing the connections requires more effort than with AESL.
# Basics
A comment starts with the character “#”.
Keywords and variables are case sensitive.
Variable names can be chosen relatively freely. Thus, same as with AESL it is recommended to use readable formulas such as “A+B”. Only the reserved words are not permitted.
Variables with the same name are connected on the wiring board.
## Reserved Words
The following expressions may not be used for variables. They may not
… start with
1*, 10*, 100*, 1000*
… contain
- <space>, <comma>
- :, #, =, ->
… be
- -1, +1
- 1, 10, 100
- *
- coefficient
- compare
- GT0
- IC
- iintegrate
- invert
- isum
- limit
- LT0
- multiply

## Syntax
Optional values are enclosed in [] brackets.
# Operations
Indentation is used to indicate parameters belonging to one operation. If this is being employed, the operation ends with “:”.
## Coefficients / Constants
There are two formats for coefficients:
coefficient(number): coefficient_name
The coefficient is referenced by coefficient_name.
This format is used to multiply a variable_name with a constant set by this coefficient.
coefficient(number): input -> coefficient_name
This is used to generate constants. input is “+1” or “-1” and thus the coefficient generates a positive or negative constant

number is the number identifier of the coefficient.
## Comparing
If variable_1 + variable_2 > 0, then variable_3 is available at variable_5, otherwise variable_4 is available.
compare (variable_1, variable_2) -> variable_5:
GT0: variable_3
LT0: variable_4
## Integration
Integrate and invert the sum of weighted input values over time.
iintegrate ([weight*]variable-1 [, …]) -> variable-n:
[IC: variable-IC]
[limit: GT0]

weight can be 1*, 10*, 100* etc. The value of the variable is multiplied by this weight. weight can be omitted for 1*.
IC is the initial condition. It has the same sign as the input. If omitted 0 is used.
limit limits the output variable-n:
- GT0: limits to values > 0.
  - this is realized by connecting the output variable-n via the cathode of a diode to the SJ-junction of the integrator. There is a small slag, thus the output takes a tiny negative value. As soon as the cathode of the diode gets negative, the input of the integrator is short-circuited to the output and inhibits further integration.
## Inverting
Invert variable_name1 giving variable_name2.
invert(variable_name1) -> variable_name2
## Multiplication
### of 2 variables
Multiply variable_x by variable_y.
multiply(variable_x, variable_y) -> variable_name
### of a variable with a constant
variable_1 * coefficient_name -> variable_2

Multiplies variable_1 with coefficient_name giving variable_2. The value of coefficient_name is in the range of [0 .. 1].
It is realized by connecting variable_1 to the corresponding coefficient.
## Summing
Sum and invert the weighted input values.
isum ([weight*]variable-1 [, …]) -> variable-n

weight can be 1*, 10* etc. The value of the variable is multiplied by this weight. weight can be omitted for 1*.