Analog Engine
Example Applications
This document includes examples of applications realized with an analog engine. The scripting language used is described in the document “Analog Engine Scripting Language”.
Author: Dietmar Hiller
Version 2023-09-24
# Mean Value
Calculates the mean value of 2 values.
The application makes use of the fact that the feedback resistor of the summing element has the same value as the input resistors to the operational amplifier. Thus, feeding back from the output to an input puts in parallel the original feedback resistor to one or more input resistors, which divides the sum by a certain value:
result = { sum from {i} (input_i * weight_i) } over {1+ sum from {j} (weight_j)}
IDENTIFICATION DIVISION
PROGRAM-ID Mean_Value

ENVIRONMENT DIVISION
ENGINE Anabrid-THAT
REQUIRES Coefficient 2
REQUIRES Summer 1
REQUIRES Inverter 1

DATA DIVISION
OUTPUT OUT_U (A+B) # The result (A+B) is routed to output u

PROGRAM DIVISION
+1 -> Coefficient.1 -> A
+1 -> Coefficient.2 -> B
A,B,-(A+B) -> Summer.1 -> -(A+B) # note the feedback doing the division by 2
-(A+B) -> Inverter.1 -> (A+B)

OPERATION DIVISION
MODE SINGLE
# Radioactive Decay
N’ = -lambda * N
IDENTIFICATION DIVISION
PROGRAM-ID Radioactive_Decay

ENVIRONMENT DIVISION
ENGINE Anabrid-THAT
REQUIRES Coefficient 2
REQUIRES Integrator 1
REQUIRES Inverter 1

DATA DIVISION
OUTPUT OUT_X N
COEFFICIENT.1 N0
COEFFICIENT.2 lambda

PROGRAM DIVISION
+1 -> Coefficient.1 -> N0
N’=-lambda*N, IC:N0 -> Integrator.1 -> -N
-N -> Coefficient.2 -> -lambda*N
-N -> Inverter.1 -> N

OPERATION DIVISION
MODE REPEAT
SPEED 20ms

Set microphone loudness to center value, oscilloscope: 5 ms/div.
# Damped Oscillator
Differential equation: my’’ + Dy’ + Sy = 0, with m the mass, D the damping with speed and S the spring constant. Rewritten to y’’=-1/m * (Dy’+Sy).
An initial condition is required; we put the deflection to y0.

IDENTIFICATION DIVISION
PROGRAM-ID Damped_Oscillator

ENVIRONMENT DIVISION
ENGINE Anabrid-THAT
REQUIRES COEFFICIENT 4
REQUIRES INTEGRATOR 2
REQUIRES INVERTER 2
REQUIRES SUMMER 1

DATA DIVISION
OUTPUT OUT_X y
COEFFICIENT.1 -y0 # -initial position
COEFFICIENT.2 S # spring force
COEFFICIENT.3 D # damping, linear to speed
COEFFICIENT.4 1/m # 1 / mass

PROGRAM DIVISION
-1 -> COEFFICIENT.1 -> -y0 # -initial position of the mass
y’’ -> INTEGRATOR.1 -> -y’
-y’,IC:-y0 -> INTEGRATOR.2 -> y
y -> COEFFICIENT.2 -> S*y # springforce times displacement
-y’ -> INVERTER.1 -> y’
y’ -> COEFFICIENT.3 -> D*y’ # damping times speed
S*y, D*y’ -> SUMMER.1 -> -(Dy’+Sy)
-(Dy’+Sy) -> COEFFICIENT.4 -> -1/m*(Dy’+Sy)=y’’

OPERATION DIVISION
MODE REPEAT
SPEED 20ms # REPF 0,200