Analog Engine
Example Applications
This document includes examples of applications realized with an analog engine. The scripting language used is described in the document “Analog Engine Scripting Language”.
Author: Dietmar Hiller
# Version History
2023-10-06	Adapt to updated syntax: OUT.U use of ALIAS / corrected usage of operation time: OP-TIME instead of SPEED	Dietmar Hiller
2023-10-04	Added damped harmonic oscillator	Dietmar Hiller
2023-09-24	First draft	Dietmar Hiller

# Helper Functions
## Adjustable Value -1 to +1
While the conection of a coefficient potentiometer to the machine units supply gives an adjustable value in a range of either [−1, 0] or [0, +1], this function offers an adjustable value within the entire machine unit range of [−1, +1].
Note, the summer is negating the output.
-1 -> Coefficient.1 -> variable
+1, variable, variable -> Summer.1 -> output
## Mean Value
Calculates the mean value of 2 values.
The application makes use of the fact that the feedback resistor of the summing element has the same value as the input resistors to the operational amplifier. Thus, feeding back from the output to an input puts in parallel the original feedback resistor to one or more input resistors, which divides the sum by a certain value:
result = { sum from {i} (input_i * weight_i) } over {1+ sum from {j} (weight_j)}
+1 -> Coefficient.1 -> A
+1 -> Coefficient.2 -> B
A,B,-(A+B)/2 -> Summer.1 -> -(A+B)/2 # note the feedback doing the division by 2
-(A+B)/2 -> Inverter.1 -> (A+B)/2
# Radioactive Decay
N’ = -lambda * N
IDENTIFICATION DIVISION
PROGRAM-ID Radioactive_Decay

ENVIRONMENT DIVISION
ENGINE Anabrid-THAT
REQUIRES Coefficient 2
REQUIRES Integrator 1
REQUIRES Inverter 1

DATA DIVISION
OUTPUT OUT.X N
ALIAS COEFFICIENT.1 InitialValue
ALIAS COEFFICIENT.2 Decay

PROGRAM DIVISION
+1 -> InitialValue -> N0
N’, IC:N0 -> Integrator.1 -> -N
-N -> Decay -> -lambda*N=N’
-N -> Inverter.1 -> N

OPERATION DIVISION
MODE REPEAT
OP-TIME 20ms

Set microphone loudness to center value, oscilloscope: 5 ms/div.
# Damped Harmonic Oscillator
Differential equation: my’’ + Dy’ + Sy = 0, with m the mass, D the damping with speed and S the spring constant. Rewritten to y’’=-1/m * (Dy’+Sy).
An initial condition is required; we put the deflection to y0 and the speed to y0’.

IDENTIFICATION DIVISION
PROGRAM-ID Damped_Oscillator

ENVIRONMENT DIVISION
ENGINE Anabrid-THAT
REQUIRES COEFFICIENT 5
REQUIRES INTEGRATOR 2
REQUIRES INVERTER 1
REQUIRES SUMMER 2

DATA DIVISION
OUTPUT OUT.U y
ALIAS COEFFICIENT.1 InitialPosition
ALIAS Coefficient.2 InitialSpeed
ALIAS COEFFICIENT.3 SpringForce
ALIAS COEFFICIENT.4 Damping # linear to speed
ALIAS COEFFICIENT.5 Mass # 1 / mass

PROGRAM DIVISION
# Colors being used for wiring
# - black: y0
# - blue: y0’
# - green: y0’’
# - yellow: y’’, y’
# - red: y
-1 -> InitialPosition -> -y0 # -initial position of the mass
-1 -> InitialSpeed -> y0s’ # y’ is scaled to be within -1..+1
+1, y0s’, y0s’ -> Summer.1 -> y0’

y’’, IC:y0’ -> INTEGRATOR.1 -> -y’
-y’,IC:-y0 -> INTEGRATOR.2 -> y
y -> SpringForce -> S*y # springforce times displacement
-y’ -> INVERTER.1 -> y’
y’ -> Damping -> D*y’ # damping times speed
S*y, D*y’ -> SUMMER.2 -> -(Dy’+Sy)
-(Dy’+Sy) -> Mass -> -1/m*(Dy’+Sy)=y’’

OPERATION DIVISION
MODE REPEAT
OP-TIME 80ms # REPF 0.800; Osci: 10 ms/div, trigger: rising at 50,