Analog Engine
Technical Topics
This document provides some insights into an analog engine including some tricks and hints for its usage.
Author: Dietmar Hiller
# Version History
2024-01-12	First version based on “Application Examples Timing topics	Dietmar Hiller

# THAT
- Voltages
  - Signals +-10 V
  - RCA-OUT X,Y,Z,U: +-1 V
- Operating time:
  - REP : 0-10s
  - REPF: 0-100 ms
- Operators
  - Summer
    - Rf = 1 MOhm (feedback resistor)
    - Ri (1) = 1 MOhm
    - Ri (10)= 100 kOhm
- Trigger
  - 5V TTL logic [0, 5V]
  - low level indicates operation
  - high level indicates halted or initial
## Time constants
The integration time scale factor k0 of the integrators is given by the product of the resistance of the input and the capacitance of the feedback.
The “1” inputs have a resistance of 1 MOhm and those scaled by “10” of 100 kOhm.
The capacitance is by default at 1 nF; by connecting SLOW to OUT a 100 nF capacitance can be put in parallel, increases the time scale factors of the respective integrator by a factor of approximately 100.
This gives the following time constant matrix for the speed of the integrator:
				speed
				normal		slow
				C=1 nF	1E-09	C=100 nF	100E-09
				Time constant	ω [kHz]	Time constant	ω [kHz]
input	1	R=1 MΩ	1E+06	1 ms	6,2832	100 ms	0,0628
	10	R=100 kΩ	100E+03	0,1 ms	62,8319	10 ms	0,6283

E.g. a time constant of 1 ms means that, if you connect a -1 signal to a “1” input, the output will ramp from 0 to 1 machine unit in 1ms.
### Sine function
In order to investigate the effect of the time constant on the output of an analog engine, a sine function was used.
It is generated by solving the differential equation
ddot x(t) = -%omega ^{2} cdot x(t) ,
which has as one solution
alignl x(t) = I0 * sin (%omega cdot t) + a0 cdot t² + v0 cdot t + x0 newline alignl dot x(t) = %omega cdot I0 cdot cos (%omega cdot t) + a0 cdot t + v0 newline alignl ddot x(t) = -%omega^2 cdot I0 cdot sin (%omega cdot t) + a0
Here, we set a0=v0=x0=0 for simplicity.
The THAT program looks like:
1 -> Coefficient.1 -> I0
x’’ -> Coefficient.6 -> xs’’
1:xs’’ -> Integrator.1 -> -x’
-x’ -> Coefficient.7 -> -xs’
1:-xs’, IC:I0 -> Integrator.2 -> x
x -> Inverter.1 -> -x
-x -> Coefficient.5 -> -omega2*x=x’’ # omega squared
The coefficients 6 and 7, and thus xs’’ and xs’, have been introduced to allow to multiply x’’ and x’ by 0,1 when a 10x input of the integrator is used in order to maintain the intended value.
The entire measurement matrix is included in this file:
The conclusion in summary,
- The 10x inputs speed up the integration. This has no effect on the frequency (omega) nor the amplitude of x’ and x.
- using SLOW divides the factor omega² by 100 per integrator used, thus the frequency is divided by root(100)=10.
- SLOW on the first integrator has no influence on the amplitudes of x’ and x.
- However, SLOW on the second integrator, additionally to the effect caused by the change of omega on x’ also multiplies the amplitude of x’ by 100.
  - I have not yet understood the mathematical reason behind this.
# Scaling
## Time
The time scale of the analog engine is governed by the time constant of the integrators. One time unit of the algorithm corresponds to the time constant (the timebase) of the engine.
For the Anabrid-THAT input resistance is 1 MΩ and the capacitance 1 nF, giving a time constant of 1 ms. This means that 1 ms of the engine corresponds to 1 time-unit of the calculation, which is 1 s if SI units are used for all variables and parameters.
To analyze a problem, this time-unit may be too slow or too fast. Thus scaling is necessary. Scaling time can be performed by describing the problem in terms of a different time unit, e.g. years for demographic applications or nano-seconds for electronic ones.
## Amplitude
All values of an analog engine always have to fall in the interval [-1, +1].
This means that initial conditions and constants have to be scaled to the engine range. Also it has to be made sure that the system during operation does not exceed this interval.
The easiest way to do scaling is to use prefixes to the SI units, so e.g. centi for 10-2 or mega for 106. Note that the entire algorithm has to be rewritten into these new units.
Best practice is to only use SI base units which are
- Meter (m) for length
- Second (s) for time
- Kilogram (kg) for mass
- Ampere (A) for electrical current
- Kelvin (K) for temperature
- Mol (mol) for amount of substance
- Candela (cd) for luminous intensity
This means that derived units should be re-written to their base units. For instance 1 N = 1 kg*m/s².
As an example, we may use the following data for the damped harmonic oscillator:
Initial Position	y0	1,5 m
Initial Speed	y0’	-0,15 m/s
Spring Force	S	2,5 N/m	kg/s²
Damping	D	0,3 N/(m/s)	kg/s
Mass	m	0,06 kg
	1/m	16,667 kg-1

Critical values are initial position (1,5 m) and 1/m (16,667 kg-1). Spring force could be coped with by using a gain 10 input.
Please see the table below while following the description of the following steps.
First we take care of y0. We replace the length measured in meter with 10¹ meter, thus we make use of deca-meter. y0 and y0’ have to be adapted. See columns “deca-m” below. Spring Force and Damping remain unchanged because in base units the length gets canceled out.
Next issue is that 1/m is well above 1. We are representing the weight by 10-2 kg, so 10¹ grams (deca-g). See columns “deca-g”. This also influences spring force and damping, which now exceed our target range.
Now, the second is replaced by 10-1 (deci-s) seconds resulting in the columns “deci-s”. Note that this also performs time-scaling, so that one time-unit of the analog engine now corresponds to one deci-second instead of one second before.
After the last scaling we have the issue that y0’ is very close to zero. There are more advanced scaling techniques which manage to optimize the value range of each operational amplifier. For instance the initial speed is converted to a value very close to zero, which is not the optimal. These can be found e.g. at
- “Analog computing using dynamic amplitude scaling and methods of use”, patent US11120230B2 Yannis Tsividis at Sendyne Corp, September 2018
- “Analog Computing Technique” by Robert Paz, Mai 1999 (link)
- “Handbook of Analog Computing” by Electronic Associates Inc.
- “Automatic Analog Computer Scaling Using Digital Optimization Techniques” by John Celmer and Mary Rouland, NASA March 1970 (link)
# Helper Functions
## Adjustable Value -1 to +1
While the connection of a coefficient potentiometer to the machine units supply gives an adjustable value in a range of either [−1, 0] or [0, +1], this function offers an adjustable value within the entire machine unit range of [−1, +1].
Note, the summer is negating the output.
-1 -> Coefficient.1 -> variable
+1, variable, variable -> Summer.1 -> output
## Mean Value
Calculates the mean value of 2 values.
The application makes use of the fact that the feedback resistor of the summing element has the same value as the input resistors to the operational amplifier. Thus, feeding back from the output to an input puts in parallel the original feedback resistor to one or more input resistors, which divides the sum by a certain value:
result = { sum from {i} (input_i * weight_i) } over {1+ sum from {j} (weight_j)}
+1 -> Coefficient.1 -> A
+1 -> Coefficient.2 -> B
A,B,-(A+B)/2 -> Summer.1 -> -(A+B)/2
    # note the feedback doing the division by 2
-(A+B)/2 -> Inverter.1 -> (A+B)/2