Language for Analog Computing Engines (LACE)
# Version History
‍2024-10-07	define: some items are optional	Dietmar Hiller
‍2024-09-09	major rework of the syntax	Dietmar Hiller
‍2024-07-24	added division, assign	Dietmar Hiller
‍2024-07-05	renamed to LACE; removed brackets for some operations; parameters are separated by space, comma or line break	Dietmar Hiller
2024-06-01	added operation output, division in isum	Dietmar Hiller
2024-05-29	First draft, still work in progress	Dietmar Hiller

License: CC BY-NC-SA 4.0 (https://creativecommons.org/licenses/by-nc-sa/4.0/ )
# Introduction
LACE (Language for Analog Computing Engines) is a scripting language for analog engines. It is focused on function, user readability and simplicity.
# Basics
## Functions
The general syntax of functions is as follows:
function-name (<parameter type>: parameter, ...) -> result
<parameter type>: parameter
<parameter type>: parameter
The brackets “()” are optional, same is the “,”.
The <parameter type> may be omitted if the allocation is unambiguous.
Parameters can be listed in brackets after the function name or separated in indented lines below. This is recommended where readability is improved.
## Comments
A comment starts with the character “#” and can be placed in a separate line or at the end of a command.
## Include
To include the code of another file use
include <filename>
This can be used if non-standard compound functions or functions realized on special external boards are needed.
## Variables
Variable names can be chosen relatively freely. Thus, it is recommended to use readable formulas such as “A+B”. Only the reserved words are not permitted.
Variables with the same name are connected on the wiring board.
Keywords and variables are case sensitive.
### Reserved Words
The following expressions may not be used for variables. They may not
… contain
- <space>, <comma>
- :, #, ->
… be
- -1, +1
- assign
- capacitor
- cmultiply
- coefficient
- compare
- connect
- define
- diode
- GND
- GT0
- idivide
- iintegrate
- include
- invert
- isum
- multiply
- output
- out.x, out.y, out.z, out.u
- zdiode
# Functions
## Assign
Assigns one variable name to another variable name. Thus both variables are equal. This is useful for the Kelvin feedback to make the output of the circuit equal to the input of the differential equation.
assign (variable_1) -> variable_2
## Coefficients
Coefficients are constants which can be set by the operator. They are recognized by an identifier, which is provided after the dot after the word coefficient.
coefficient.<identifier> [(constant)] -> name

If the constant is given, which can be -1 or +1, the coefficient is generating a constant with name name which can be used e.g. as initial condition for integration.
Omitting the constant, the coefficient is used to cmultiply a variable with the value set by that coefficient.
It is advised to have all coefficients listed at the top of the code. This eases changes if e.g. the identifier of coefficients has to change.Comparing
If variable_A + variable_B > 0, then variable_GT0 is available at result, otherwise variable_LT0 is available.
compare (A: variable_A, B: variable_B) -> result
GT0: variable_GT0
LT0: variable_LT0
## Integration
This performs an inverted integration of the sum of weighted input values over time int left( sum from{i} weight_i * variable_i right) dt = result .
iintegrate (weight*: variable-1, …) -> variable-n
IC: variable-IC
[SJ: …]
weight can be 1*:, 10*:, 100*: etc. The value of the variable is multiplied by this weight. weight can be omitted for 1*:.
IC is the initial condition. It has the same sign as the input. If omitted 0 is used.
SJ stands for summing junction. It is used for the implementation of compound functions.
## Inverting
inverts the sign of variable giving result: left( -variable = result right) .
invert (variable) -> result
## Multiplication
### of 2 variables
calculates the product of variable_x with variable_y left( variable_x * variable_y = result right) .
multiply (x: variable_x, y: variable_y) -> result
### of a variable with a constant
cmultiply (variable_x, variable_y) -> result

One of the 2 variables has to be a constant defined by coefficient.
## Summing
isum calculates the inverted sum of the weighted input values sum from{i} weight_i * variable_i = -result .
isum (weight*: variable-1, …) -> -result
[SJ: …]
[FB: …]

weight can be 1*:, 10*: etc. The value of the variable is multiplied by this weight. weight can be omitted for 1*:.
SJ stands for summing junction. It is used for the implementation of compound functions.
FB goes to the feedback line. It is used for the implementation of compound functions, in particular to generate an open amplifier.
## Output
Describes variables which are connected to the output of the engine.
output(variable) -> <output_identifier>

<output_identifier> can be e.g. out.x, out.y, out.z, out.u.
# Compound Functions
It may be necessary to use functions which are not readily implemented on the analogue engine, but which can be set up using on- or off-board components.
In order to increase simplicity and readability to the users, compound functions can be defined using the define function:
define function (<parameter type>: [variable-name] [, ...])
[-> result]
<definition>

The definition is a series of LACE-commands. For examples see below.
If the new function is already either intrinsically or explicitly defined, any subsequent define replaces the previous definition.
## Components
Some components may be needed to assemble compound functions.
### Connection
The connect function serves to indicate a direct connection between 2 ports.
connect (port1) -> port2
### Capacitors
Capacitors are available with different capacitances. It’s value is the identifier:
capacitor.capacitance (input) -> output
### Diodes
diodes
diode (port: input) -> output

Ports are:
    • AN: anode (+)
    • CAT: cathode (-)
### Zener-Diodes
Zener diodes
zdiode (port: input) -> output

Ports are:
    • AN: anode (+)
    • CAT: cathode (-)
## Open Amplifier
The open amplifier can be used to generate further functionality.
It is realized by connecting the FB-port of a summer to GND.
define openamp (weight*: variable-1, …) -> output
isum (weight*: variable-1, …) -> output
connect (FB:) -> GND
## Division
Divide variable_1 by variable_2 giving result left( frac {variable_1} {variable_2} = -result right) . Note the inverted sign of the result due to the usage of an open amplifier.
It is realized by placing a multiplier in the return path of an openamp.
define idivide (variable_1, variable_2) -> -result
openamp (variable_1, OA) -> -result
multiply -result, variable_2 -> OA
## Integration
### Extension
This adds some additional functionality to the integration command:
define iintegrate (weight*: variable-1, …, IC: variable-IC,
limit: GT0) -> variable-n
iintegrate (weight*: variable-1, …) -> variable-n
diode (CAT:	variable-n) -> DA
connect (DA) -> SJ:

limit limits the output variable-n:
- GT0: limits to values > 0.
  - As soon as the cathode of the diode gets negative, the input of the integrator is short-circuited to the output and inhibits further integration.
  - There is a small slag, thus the output takes a tiny negative value.
### Built with Openamp
Additional integrators can be built with an openamp
define iintegrate.additional (variable) -> integral
   openamp (variable) -> integral
      connect (SJ:) -> cp
   capacitor.100nF (integral) -> cp
The 100 nF capacitor is available on a THAT. This capacitance corresponds to those of the SLOW settings. In order to use the standard time constant an external 1 nF capacitor has to be used.
## Summing Extension
This extension adds the possibility to divide the sum by a small integer
define isum (weight*: variable-1, …, DIV: divisor) -> -result
isum (weight*: variable-1, …) -> -result
connect (-result, …) -> 1*:
...

divisor can be 2, 3, …. Each connect increases the divisor by the value of the corresponding weight.