Analog Engine
Example Applications
This document includes examples of applications realized with an analog engine. The scripting language used is described in the document “Analog Engine Scripting Language”.
Author: Dietmar Hiller
# Version History
2023-11-02	Analytical solution of the damped harmonic oscillator / Scaling amplitude and time	Dietmar Hiller
2023-10-06	Adapt to updated syntax: OUT.U use of ALIAS / corrected usage of operation time: OP-TIME instead of SPEED	Dietmar Hiller
2023-10-04	Added damped harmonic oscillator	Dietmar Hiller
2023-09-24	First draft	Dietmar Hiller

# Helper Functions
## Adjustable Value -1 to +1
While the connection of a coefficient potentiometer to the machine units supply gives an adjustable value in a range of either [−1, 0] or [0, +1], this function offers an adjustable value within the entire machine unit range of [−1, +1].
Note, the summer is negating the output.
-1 -> Coefficient.1 -> variable
+1, variable, variable -> Summer.1 -> output
## Mean Value
Calculates the mean value of 2 values.
The application makes use of the fact that the feedback resistor of the summing element has the same value as the input resistors to the operational amplifier. Thus, feeding back from the output to an input puts in parallel the original feedback resistor to one or more input resistors, which divides the sum by a certain value:
result = { sum from {i} (input_i * weight_i) } over {1+ sum from {j} (weight_j)}
+1 -> Coefficient.1 -> A
+1 -> Coefficient.2 -> B
A,B,-(A+B)/2 -> Summer.1 -> -(A+B)/2 # note the feedback doing the division by 2
-(A+B)/2 -> Inverter.1 -> (A+B)/2
# Radioactive Decay
N’ = -lambda * N
IDENTIFICATION DIVISION
PROGRAM-ID Radioactive_Decay

ENVIRONMENT DIVISION
ENGINE Anabrid-THAT
REQUIRES Coefficient 2
REQUIRES Integrator 1
REQUIRES Inverter 1

DATA DIVISION
OUTPUT OUT.X N
ALIAS COEFFICIENT.1 InitialValue
ALIAS COEFFICIENT.2 Decay

PROGRAM DIVISION
+1 -> InitialValue -> N0
N’, IC:N0 -> Integrator.1 -> -N
-N -> Decay -> -lambda*N=N’
-N -> Inverter.1 -> N

OPERATION DIVISION
MODE REPEAT
OP-TIME 20ms

Set microphone loudness to center value, oscilloscope: 5 ms/div.
# Damped Harmonic Oscillator
The equation of motion for a viscously damped simple harmonic oscillator is m ddot{y} + D dot{y} + S y = 0 , with m the mass, D the damping with speed and S the spring constant.
Rewritten to y’’=-1/m * (Dy’+Sy).
An initial condition is required; we put the deflection to y0 and the speed to y0’.

IDENTIFICATION DIVISION
PROGRAM-ID Damped_Oscillator

ENVIRONMENT DIVISION
ENGINE Anabrid-THAT
REQUIRES COEFFICIENT 5
REQUIRES INTEGRATOR 2
REQUIRES INVERTER 1
REQUIRES SUMMER 2

DATA DIVISION
OUTPUT OUT.U y
ALIAS COEFFICIENT.1 InitialPosition
ALIAS COEFFICIENT.2 InitialSpeed
ALIAS COEFFICIENT.3 SpringForce
ALIAS COEFFICIENT.4 Damping # linear to speed
ALIAS COEFFICIENT.5 Mass # 1 / mass

PROGRAM DIVISION
# Colors being used for wiring
# - black: y0
# - blue: y0’
# - green: y0’’
# - yellow: y’’, y’
# - red: y
-1 -> InitialPosition -> -y0 # -initial position of the mass
-1 -> InitialSpeed -> y0s’ # y’ is scaled to be within -1..+1
+1, y0s’, y0s’ -> Summer.1 -> y0’
y’’, IC:y0’ -> INTEGRATOR.1 -> -y’
-y’,IC:-y0 -> INTEGRATOR.2 -> y
y -> SpringForce -> S*y # springforce times displacement
-y’ -> INVERTER.1 -> y’
y’ -> Damping -> D*y’ # damping times speed
S*y, D*y’ -> SUMMER.2 -> -(Dy’+Sy)
-(Dy’+Sy) -> Mass -> -1/m*(Dy’+Sy)=y’’

OPERATION DIVISION
MODE REPEAT
OP-TIME 80ms
## Analytical Solution
[https://brilliant.org/wiki/damped-harmonic-oscillators/ ]
Solutions of the viscously damped simple harmonic oscillator should be oscillations within some form of damping envelope. Ansatz is an exponential damping envelope of an oscillation:
y(t) = Ae^{-g t} e^{iat} = Ae^{t (ai-g)} = Ae^{rt}
where A is some constant and (r = ai-g) will be found. g and a are place holders to show the damping (g) and oscillation (a). Plugging this ansatz into the equation of motion yields:
(mr^2 + D r + S)Ae^{rt} = 0 newline drarrow r^2 + frac{D}{m} r + frac{S}{m} = 0
which is a quadratic equation in r with solutions:
r = - {frac{D}{2m}} +-i cdot sqrt{ {frac{S}{m}} - frac{D^2}{4m^2} }
Note that there are two roots r to the quadratic corresponding to the two general solutions:
y(t) = a_1 e^{-frac{D}{2m} t} e^{ i sqrt{{frac{S}{m}} - frac{D^2}{4m^2} }t} + a_2 e^{-frac{D}{2m} t} e^{ -i sqrt{{frac{S}{m}} - frac{D^2}{4m^2} }t}.
These solutions in general describe oscillation at frequency %omega = sqrt{{frac{S}{m}} - frac{D^2}{4m^2} } within a decay envelope of time-dependent amplitude %alpha(t) = e^{-frac{D}{2m} t} .
Note, the frequency of the oscillations is only depending on the spring constant, damping and mass, whereas the damping also depends on the mass.
For the undamped case (D=0) this gives
alignl y(t) = a_1 e^{i %omega t} + a_2 e^{-i %omega t} newline alignl y(t) = a_1 cdot (cos (%omega t) + i sin (%omega t)) + a_2 cdot (cos (%omega t) - i sin (%omega t)) newline alignl y(t) = (a_1 + a_2) cdot cos(%omega t) + i (a_1 - a_2) sin (%omega t) newline alignc a_1 + a_2 = A newline alignc i(a_1 - a_2) = B newline alignl y(t) = A cos(%omega t) + B sin(%omega t) newline alignc y(t=0) = y_0 = A newline alignc dot y(t=0) = v_0 = B %omega newline alignl y(t) = y_0 cos(%omega t) + frac{v_0}{%omega} sin(%omega t)
This can also be written as
alignl y(t)=b cdot cos(%omega t - %varphi) newline alignc "because of" newline alignc y(t)=b cdot (cos(%omega t) cdot cos (%varphi) + sin(%omega t) cdot sin(%varphi) ) newline alignc y(t)=b cdot cos(%varphi) cdot cos(%omega t) + b cdot sin(%varphi) cdot sin(%omega t) newline alignc "with" newline alignc x_0 = b cdot cos(%varphi) newline alignc frac{v_0}{%omega} = b cdot sin(%varphi)

## Scaling
### Time
The time scale of the analog engine is governed by the time constant of the integrators. One time unit of the algorithm corresponds to the time constant (the timebase) of the engine.
For the Anabrid-THAT input resistance is 1 MΩ and the capacitance 1 nF, giving a time constant of 1 ms. This means that 1 ms of the engine corresponds to 1 time-unit of the calculation, which is 1 s if SI units are used for all variables and parameters.
To analyze a problem, this time-unit may be too slow or too fast. Thus scaling is necessary. Scaling time can be performed in various ways:
1. Describe the problem in terms of a different time unit, e.g. years for demographic applications or nano-seconds for electronic ones.
2. Many engines have the possibility to place another capacitor in parallel to the standard one. This increases the time constant, thus the timebase of the engine. Anabrid-THAT e.g. places in SLOW-Mode a 100 nF capacitance in parallel thus the timebase becomes 101 ms.
   Note that all integrators used have to be running in the same mode, i.e. NORMAL or SLOW. In mixed mode the result may be inconsistent.
3. The 10x input of the integrators have a resistance of 1/10 of the 1x inputs. Thus the time constant is divided by 10 so that for the Anabrid-THAT 100 µs correspond to 1 time unit of the algorithm.
  - The same effect can be obtained by multiplying all inputs to every integrator by a factor of 10.
### Amplitude
All values of an analog engine always have to fall in the interval [-1, +1].
The example code above is good for a qualitative analysis of a problem but real life values usually do not fall into this range. This means that initial conditions and constants have to be scaled to the engine range. Also it has to be made sure that the system during operation does not exceed this interval.
The easiest way to do scaling is to use prefixes to the SI units, so e.g. centi for 10-2 or mega for 106. Note that the entire algorithm has to be rewritten into these new units.
Best practice is to only use SI base units which are
- Meter (m) for length
- Second (s) for time
- Kilogram (kg) for mass
- Ampere (A) for electrical current
- Kelvin (K) for temperature
- Mol (mol) for amount of substance
- Candela (cd) for luminous intensity
This means that derived units should be re-written to their base units. For instance 1 N = 1 kg*m/s².
As an example, we may use the following data for the damped harmonic oscillator:
Initial Position	y0	1,5 m
Initial Speed	y0’	-0,15 m/s
Spring Force	S	2,5 N/m	kg/s²
Damping	D	0,3 N/(m/s)	kg/s
Mass	m	0,06 kg
	1/m	16,667 kg-1

Critical values are initial position (1,5 m) and 1/m (16,667 kg-1). Spring force could be coped with by using a gain 10 input.
Please see the table below while following the description of the following steps.
First we take care of y0. We replace the length measured in meter with 10¹ meter, thus we make use of deca-meter. y0 and y0’ have to be adapted. See columns “deca-m” below. Spring Force and Damping remain unchanged because in base units the length gets canceled out.
Next issue is that 1/m is well above 1. We are representing the weight by 10-2 kg, so 10¹ grams (deca-g). See columns “deca-g”. This also influences spring force and damping, which now exceed our target range.
Now, the second is replaced by 10-1 (deci-s) seconds resulting in the columns “deci-s”. Note that this also performs time-scaling, so that one time-unit of the analog engine now corresponds to one deci-second instead of one second before.
After the last scaling we have the issue that y0’ is very close to zero. There are more advanced scaling techniques which manage to optimize the value range of each operational amplifier. For instance the initial speed is converted to a value very close to zero, which is not the optimal. These can be found e.g. at
- “Analog computing using dynamic amplitude scaling and methods of use”, patent US11120230B2 Yannis Tsividis at Sendyne Corp, September 2018
- “Analog Computing Technique” by Robert Paz, Mai 1999 (link)
- “Handbook of Analog Computing” by Electronic Associates Inc.
- “Automatic Analog Computer Scaling Using Digital Optimization Techniques” by John Celmer and Mary Rouland, NASA March 1970 (link)
The fully scaled program thus is as follows. Note that the gain 10 inputs are used for SUMMER.2 in order to achieve damping and spring constant values:
IDENTIFICATION DIVISION
PROGRAM-ID Damped_Oscillator

ENVIRONMENT DIVISION
ENGINE Anabrid-THAT
TIMEBASE 1ms
REQUIRES COEFFICIENT 5
REQUIRES INTEGRATOR 2
REQUIRES INVERTER 1
REQUIRES SUMMER 2

DATA DIVISION
OUTPUT OUT.U y
ALIAS COEFFICIENT.1 InitialPosition
ALIAS COEFFICIENT.2 InitialSpeed
ALIAS COEFFICIENT.3 SpringForce
ALIAS COEFFICIENT.4 Damping # linear to speed
ALIAS COEFFICIENT.5 Mass # 1 / mass

PROGRAM DIVISION
# Colors being used for wiring
# - black: y0
# - blue: y0’
# - green: y0’’
# - yellow: y’’, y’
# - red: y
-1 -> InitialPosition -> -y0 # -initial position of the mass
-1 -> InitialSpeed -> y0s’ # y’ is scaled to be within -1..+1
+1, y0s’, y0s’ -> Summer.1 -> y0’

y’’, IC:y0’ -> INTEGRATOR.1 -> -y’
-y’,IC:-y0 -> INTEGRATOR.2 -> y
y -> SpringForce -> S*y # springforce times displacement
-y’ -> INVERTER.1 -> y’
y’ -> Damping -> D*y’ # damping times speed
10:S*y, 10:D*y’ -> SUMMER.2 -> -(Dy’+Sy)
-(Dy’+Sy) -> Mass -> -1/m*(Dy’+Sy)=y’’

OPERATION DIVISION
MODE REPEAT
OP-TIME 57ms

Obtained damped oscillation with parameters above
Adapted parameters: D=1,69, y0'=-0,187; calculated T=9,97 ms