Analog Engine
Example Applications
This document includes examples of applications realized with an analog engine. The scripting language used is described in the document “Analog Engine Scripting Language”.
Author: Dietmar Hiller
License: CC BY-NC-SA 4.0 (https://creativecommons.org/licenses/by-nc-sa/4.0/ )
# Version History
‍2024-05-29	Applications: Hollow Cylinder; Rope on Edge of Table	Dietmar Hiller
‍2024-02-25	Application: Falling Mass	Dietmar Hiller
‍2024-02-16	Application: Mass in Tube	Dietmar Hiller
‍2024-02-05	Application: Comet on parabolic orbit	Dietmar Hiller
‍2024-02-01	Harmonic Oscillator basics	Dietmar Hiller
‍2024-01-31	corrected 10¹ is da (deca) / License CC BY-NC-SA / Application: 2 raindrops	Dietmar Hiller
‍2024-01-24	Some general details / Mass at the apex on a sphere	Dietmar Hiller
‍2024-01-16	Added: Mass with charge in e/m field	Dietmar Hiller
2024-01-08	Separated Helper Functions and Scaling to “Technical Topics” / Moved code to separate files AESL / Analytical solution of the damped harmonic oscillator / Scaling amplitude and time	Dietmar Hiller
2023-10-06	Adapt to updated syntax: OUT.U use of ALIAS / corrected usage of operation time: OP-TIME instead of SPEED	Dietmar Hiller
2023-10-04	Added damped harmonic oscillator	Dietmar Hiller
2023-09-24	First draft	Dietmar Hiller

# Example Applications
## Radioactive Decay
N’ = -lambda * N
+1 -> InitialValue -> N0
N’, IC:N0 -> INTEGRATOR -> -N
-N -> Decay -> -lambda*N=N’
-N -> INVERTER -> N

Note that the integrator is inverting the sign and that the initial condition has the same sign as the input.
Full code see “Radioactive Decay.AESL”
## Harmonic Oscillator
### Undamped
A mass m is subject to a force vec F = - k vec r .
The equation of motion is
alignl m ddot vec r = -k vec r newline so newline alignl m ddot x = -k x ~ -> ~ ddot x = - {k over m} x newline alignl m ddot y = -k y ~ -> ~ ddot y = - {k over m} y newline
z can be set to zero.
The application is straight forward, see “TP1 04.12 Harmonic Oscialltor.AESL”.
k/m is arbitrarily set to 0,541, a to 0,568.

What is its trajectory if the mass starts at position (a,0,0)?
  - The trajectory is a sine oscillation.
At which time does it pass through (0,0,0)?
  - It passes through (0,0,0) at 2,135 s (timebase is 1 ms which corresponds to 1 s of the application).
    This is in accordance to the calculated value of %tau = %pi over 2 sqrt{m over k} = 2,136 s .
What is its trajectory if it has additionally the initial speed (0,v0,0)?
  - It is ellipsoidal. Here v0=0,122 was used.

### Damped
The equation of motion for a viscously damped simple harmonic oscillator is m ddot{y} + D dot{y} + S y = 0 , with m the mass, D the damping with speed and S the spring constant.
Rewritten to y’’=-1/m * (Dy’+Sy).
An initial condition is required; we put the deflection to y0 and the speed to y0’.
Full code see “Damped Harmonic Oscillator.AESL”
#### Analytical Solution
[https://brilliant.org/wiki/damped-harmonic-oscillators/ ]
Solutions of the viscously damped simple harmonic oscillator should be oscillations within some form of damping envelope. Ansatz is an exponential damping envelope of an oscillation:
y(t) = Ae^{-g t} e^{iat} = Ae^{t (ai-g)} = Ae^{rt}
where A is some constant and (r = ai-g) will be found. g and a are place holders to show the damping (g) and oscillation (a). Plugging this ansatz into the equation of motion yields:
(mr^2 + D r + S)Ae^{rt} = 0 newline drarrow r^2 + frac{D}{m} r + frac{S}{m} = 0
which is a quadratic equation in r with solutions:
r = - {frac{D}{2m}} +-i cdot sqrt{ {frac{S}{m}} - frac{D^2}{4m^2} }
Note that there are two roots r to the quadratic corresponding to the two general solutions:
y(t) = a_1 e^{-frac{D}{2m} t} e^{ i sqrt{{frac{S}{m}} - frac{D^2}{4m^2} }t} + a_2 e^{-frac{D}{2m} t} e^{ -i sqrt{{frac{S}{m}} - frac{D^2}{4m^2} }t}.
These solutions in general describe oscillation at frequency %omega = sqrt{{frac{S}{m}} - frac{D^2}{4m^2} } within a decay envelope of time-dependent amplitude %alpha(t) = e^{-frac{D}{2m} t} .
Note, the frequency of the oscillations is only depending on the spring constant, damping and mass, whereas the damping also depends on the mass.
For the undamped case (D=0) this gives
alignl y(t) = a_1 e^{i %omega t} + a_2 e^{-i %omega t} newline alignl y(t) = a_1 cdot (cos (%omega t) + i sin (%omega t)) + a_2 cdot (cos (%omega t) - i sin (%omega t)) newline alignl y(t) = (a_1 + a_2) cdot cos(%omega t) + i (a_1 - a_2) sin (%omega t) newline alignc a_1 + a_2 = A newline alignc i(a_1 - a_2) = B newline alignl y(t) = A cos(%omega t) + B sin(%omega t) newline alignc y(t=0) = y_0 = A newline alignc dot y(t=0) = v_0 = B %omega newline alignl y(t) = y_0 cos(%omega t) + frac{v_0}{%omega} sin(%omega t)
This can also be written as
alignl y(t)=b cdot cos(%omega t - %varphi) newline alignc "because of" newline alignc y(t)=b cdot (cos(%omega t) cdot cos (%varphi) + sin(%omega t) cdot sin(%varphi) ) newline alignc y(t)=b cdot cos(%varphi) cdot cos(%omega t) + b cdot sin(%varphi) cdot sin(%omega t) newline alignc "with" newline alignc x_0 = b cdot cos(%varphi) newline alignc frac{v_0}{%omega} = b cdot sin(%varphi)

#### Scaling
As an example, we may use the following data for the damped harmonic oscillator:
Initial Position	y0	1,5 m
Initial Speed	y0’	-0,15 m/s
Spring Force	S	2,5 N/m	kg/s²
Damping	D	0,3 N/(m/s)	kg/s
Mass	m	0,06 kg
	1/m	16,667 kg-1

Critical values are initial position (1,5 m) and 1/m (16,667 kg-1). Spring force could be coped with by using a gain 10 input.
Please see the table below while following the description of the following steps.
First we take care of y0. We replace the length measured in meter with 10¹ meter, thus we make use of deca-meter. y0 and y0’ have to be adapted. See columns “deca-m” below. Spring Force and Damping remain unchanged because in base units the length gets canceled out.
Next issue is that 1/m is well above 1. We are representing the weight by 10-2 kg, so 10¹ grams (deca-g). See columns “deca-g”. This also influences spring force and damping, which now exceed our target range.
Now, the second is replaced by 10-1 (deci-s) seconds resulting in the columns “deci-s”. Note that this also performs time-scaling, so that one time-unit of the analog engine now corresponds to one deci-second instead of one second before.
After the last scaling we have the issue that y0’ is very close to zero. There are more advanced scaling techniques which manage to optimize the value range of each operational amplifier. For instance the initial speed is converted to a value very close to zero, which is not the optimal.
The fully scaled program can be found at “Damped Harmonic Oscillator scaled.AESL”. Note that the gain 10 inputs are used for SUMMER.2 in order to achieve damping and spring constant values:

Obtained damped oscillation with parameters above
Adapted parameters: D=1,69, y0'=-0,187; calculated T=9,97 ms
### Hollow Cylinder
A homogeneous hollow cylinder (mass m, ration inner to outer radius ε) is connected to a massless spring (constant λ). The system is deflected from its rest position by the distance a. The cylinder rolls without sliding.
Using the energy to obtain the equation of motion.
alignl E_tot = E_kin + T^(r) + U_spring newline alignl with E_kin: kinetic energy, T^(r): energy of rotation, U_spring: energy of spring newline alignl E_tot = 1 over 2 m {dot x}^2 + 1 over 2 J %omega^2 + 1 over 2 %lambda x^2 newline ~ using J=1 over 2 m r^2 (1+ %varepsilon^2) "and" {dot x}^2 = r^2 %omega^2 newline alignl E_tot = 1 over 2 m left(1 + 1 over 2 left(1+%varepsilon^2 right) right) {dot x}^2 + 1 over 2 %lambda x^2 newline alignl "total energy is constant thus" {%delta E_tot} over {%delta t} = 0 newline alignl 0 = ddot x + {2 %lambda} over {m (3+%varepsilon^2)} x newline alignl ddot x = - left( {2 %lambda} * {1 over m} * {1 over {3+%varepsilon^2}} right) x
Script: “TP1 08.22 Hollow Cylinder.AESL”
The various configurations are shown below:
Case “tiny wall” has an infinitesimally small wall thickness, “full” is a full cylinder. Same as “70% empty” all have the same mass, thus the density varies accordingly. The last case “70% empty (d)” has the same density as “full” thus the mass is reduced, which results in a reduction of the periodicity.
Periodicity is calculated as T= %pi sqrt{2m over %lambda} sqrt{3+%varepsilon^2} . Note that the timebase of the analog engine is 1 ms, which corresponds to 1 s in the real world.
## Rope on Edge of Table
A rope (length l) slides frictionlessly down the edge of a table. Using the Lagrange-formalism to solve this problem.
alignl L = T - U newline T = 1/2 m {dot x}^2 newline f(r) = - {dU} over {dr} = %rho x g drarrow U(x) = -1/2 %rho x^2 g newline L = 1/2 m {dot x}^2 + 1/2 %rho x^2 g
The equation of motion is generated through the Euler-Lagrange equation.
Intial speed x0'=0; initial length over the edge x0=0,124; g/l=0,383
alignl {partial L} over {partial x} - d over {dt} left( {partial L} over {partial dot x} right) = 0 newline alignl {partial} over {partial x} left[ 1/2 m {dot x}^2 + 1/2 %rho x^2 g right] - d over {dt} left[ {partial} over {partial dot x} left( 1/2 m {dot x}^2 + 1/2 %rho x^2 g right) right] newline alignl %rho x g - m ddot x = 0 newline alignl ddot x = g / l cdot x
The analytical solution is x(t) = x0 cdot cosh ( sqrt(g/l) t) .
Script: “TP1 09.26 rope over table edge.DELACE”

## Mass with charge in em field
A mass m with charge q>0 is located in a static electro-magnetic field [0,0,E], [0,-B,0]. Calculate the trajectory of the mass. The Lorentz-force is causing the motion of the mass.
alignl m ddot vec r = q (vec E + vec v times vec B) newline alignl m left [ stack{ddot x # ddot y # ddot z} right ] = q left ( left [stack{0 # 0 # E} right ] + left[ stack{v_x # v_y # v_z} right] times left[ stack{0 # -B # 0} right] right ) = ~ q left ( left [stack{0 # 0 # E} right ] + left[ stack{v_z B # 0 # -v_x B} right ] right) = ~ q left ( left [stack{v_z B # 0 # E -v_x B} right ] right) .
Which results in the two differential equations
alignl ddot x = {q} over {m} dot z B newline alignl ddot z = {q} over {m} (E -dot x B) = q over m E - %omega dot x newline with %omega := q over m B , ~ a := {m E} over {q B^2} = {q E} over {%omega^2 m} newline alignl ddot x = %omega dot z newline alignl ddot z = a %omega^2 - %omega dot x newline
with the solutions
alignl x(t) = a (%omega t - sin (%omega t)) ~ rightarrow dot x(t) = a %omega (1- cos (%omega t)) ~ rightarrow ddot x(t) = a %omega^2 sin (%omega t) newline newline alignl z(t) = -a cos(%omega t) + z_0 newline with z(0)=0 newline alignl z(t) = a (1- cos(%omega t)) ~ rightarrow dot z(t) = a %omega sin (%omega t) ~ rightarrow ddot z(t) = a %omega^2 cos (%omega t) newline
This is the trajectory of a cycloid.
The AESL-program can be found in file “TP1 03.08 Charge in em field.AESL”.
It is interesting and easy to play with initial speed conditions.
Trajectory of a charge mass in an em field (omega=0,92; a*omega²=0,05; OP-time=0,21ms)	Added initial speed in x and z-direction

## Mass at the apex on a sphere
A mass m rests at the apex on a fixed sphere with radius a. With a slight displacement, it slides down the sphere without friction.
We are making use of Lagrange equations of the 1st kind.
### Equations of motion
alignl m vec ddot r = m vec g + 2 %lambda(x,y) newline alignc "so" newline alignl m ddot x = 2 %lambda x newline alignl m ddot y = 2 %lambda y - m g newline alignc "with the motion forced to the sphere" newline %varphi = x^2 + y^2 - a^2 = 0 ~->~ ddot %varphi = {dot x}^2 + x ddot x + {dot y}^2 + y ddot y = 0
### Calculating λ
Insertion of the equations of motion
alignl {dot x}^2 + x {2 %lambda x} over m + {dot y}^2 + y left( {2 %lambda y - m g} over m right) = 0 newline alignl {dot x}^2 + {dot y}^2 + {2 %lambda} over m left( x^2 + y^2 right)- g y = 0 newline alignl v^2 + {2 %lambda} over m a^2 - g y = 0 newline alignl %lambda = m over {2 a^2} left( g y - v^2 right)
v² is determined by the law of conservation of energy
E = 1 over 2 m v^2 + m g y = m g a newline v^2 = 2 g (a - y) newline alignl %lambda = m over {2 a^2} left( g y - left( 2 g (a - y) right) right) ~=~ {m g} over {2 a^2} left( 3y - 2a right)
### Final equations of motion
alignl m ddot x = 2 left( {m g} over {2 a^2} left( 3y - 2a right) right) x newline alignl m ddot y = 2 left( {m g} over {2 a^2} left( 3y - 2a right) right) y - m g newline alignl ddot x = {3 g} over a^2 x y - {2 g} over a x newline alignl ddot y = {3 g} over a^2 y^2 - {2 g} over a y - g
### Program
Scaling is done simply by using da-m (10¹ m) instead of meter in order to have g=0,981 da-m/s². Thus also a, x, y are measured in da-m. The constants are thus:
‍Const	Coefficient	Example	Unit
a		1,000	da-m
g	C5	0,981	da-m / s²
3 g / a²	C1 (for x*y), C2 (for y^2)	2,943	1 / (da-m * s²)
2 g / a	C3 (for x), C4 (for y)	1,962	1 / s²
x0	C6 (=root(a² – y0²))	0,957	da-m
y0	C7	0,290	da-m

The display of the oscilloscope is extremely sensitive to these parameters and the tolerances of the potentiometers. E.g. C6=1 had to be set to get a good result.
The full program can be found in file
“TP1 04.10 MassOnSphere.AESL”
## Two raindrops
Two raindrops of same size and altitude are falling towards the earth. How long does it take until they touch due to the gravitational force between them?
As this is a multi-body problem, we make use of the reduced mass (1/µ = 1/m1 + 1/m2). This gives the differential equation
µ ddot s = - {%gamma m_1 m_2} over s^2
With m1=m2: µ=m/2, with m=m1=m2 thus
m over 2 ddot s = - {%gamma m^2} over s^2 ~ -> ~ ddot s = - 2 {%gamma m} over s^2 .
The fact that the mass is divided by 2 can be understood by the fact that both raindrops are attracting each other, thus reducing inertia.
### Scaling
Looking at the values for this calculation, the need for scaling is evident:
- Radius of the raindrops: r=1mm
- Initial distance: 2 mm
- Constant of gravity: γ=6,672*10-11 m³/(kg s²)
- Density of water: ρ=1 kg / dm³
- Mass: m=4π/3*ρ*r³=4,189*10-6 kg

First, cm are used for the lengths, which also puts the size of the drops to a usable value. However, the constant of gravity still remains too small. Next, time is measured in 10⁴ s.

Which gives the settings:
- 2r	0,200 cm
- s0	0,400 cm
- 2gamma*m	0,056 cm³/(10^4 s)²
Timescale is: 1 Timebase = 10⁴ s
### Measurement
The time until the two drops touch is measured to 975 µs.
Timebase of THAT is 1 ms, thus the measured time is 10⁴ s * 0,975 ms / 1 ms = 9750 s = 2,71 h, which corresponds to the calculated value.
AESL-Script: “TP1 04.11 TwoRaindrops.AESL”
## Comet on parabolic orbit
A comet moves on a parabolic orbit in the gravitational field of the stationary sun. Its orbital plane coincides with the plane of the Earth's orbit, which is assumed to be circular. The perihelion distance is one third of the Earth's orbital radius RE.
How long does the comet move within the Earth's orbit?
Placing the origin into the center of gravity and making use of the reduced mass
(1/µ = 1/m1 +  1/m2), the angular momentum and energy are
alignl vec L = %mu (vec r times vec v_r) = const newline alignl E = 1/2 %mu {vec v_r}^2 + U(r) = const .
We are using plane polar coordinates
alignl vec L = %mu(r vec e_r times (dot r vec e_r + r dot %varphi vec e_%varphi)) = %mu r^2 dot %varphi vec e_z = const newline alignl E = 1/2 %mu (dot r vec e_r + r dot %varphi vec e_%varphi)^2 + U(r) = 1/2 %mu ({dot r}^2 + r^2 {dot %varphi}^2)^2 + U(r) = const newline alignc "replacing" dot %varphi " through " vec L newline alignl E = 1/2 %mu {dot r}^2 + L^2 over {2 %mu r^2} + U(r) newline alignc "rearranging to get " dot r newline alignl dot r = dr over dt = +- sqrt{2 over %mu (E - (U(r) + L^2 over {2 %mu r^2}))} newline alignc "rearranging again to get t(r)" newline alignl t(r) = +- int {1 over {sqrt{2 over %mu (E - (U(r) + L^2 over {2 %mu r^2}))}}dr} + t_0
As the comet is moving on a parabolic trajectory, total energy E=0. The potential U(r) is given by gravity. At the perihelion L can be expressed by r=1/3 RE and ̇r=0. Putting all together gives
L^2 =%mu^2 (2 %gamma m 1/3 R_E) .
m is the total mass of the sun plus the comet, which can be approximated by the mass of the sun only.
The integral has to be calculated from the entrance point RE to the exit point at RE, but due to symmetry we can use the double of the time from the entrance point to the perihelion 1/3 RE. The integral is negative due to the attraction force.
alignl t(r) = - 2 int from R_E to {1/3R_E} {1 over {sqrt{2 over %mu (- (- %gamma {%mu m} over r + {2/3 %mu^2 %gamma m R_E} over {2 %mu r^2}))}}dr} newline alignl t(r) = -sqrt{2 over {%gamma m}} int from R_E to {1/3R_E} {{1} over {sqrt{((1 over r - {R_E} over {3r^2}))}}dr} ~ = sqrt{2 over {%gamma m}} int from {1/3R_E} to {R_E} {r over {sqrt{r - 1/3 R_E}}dr}
This is an integral which can be solved with the analog engine.
### Scaling
Scaling is performed through choosing the proper SI unit prefixes. Here tera meters and 10 kilo days.

### Measurement
AESL script is in “TP1 05.15 Comet.AESL”.
Note that the input to calculating the root is limited to negative values. It was observed an a THAT that positive values, even electro-static spikes, cause the multiplier to error out which could only be reset by un- and re-plugging the inputs to the multiplier. Thus whenever the result was unexpected, this type of reset was necessary.
The integral reaches its maximum (which is the desired value) at 7,4 mV, corresponding to 7,4 * 10-3 * (10 kd)= 74 days.
The calculated value is 74,78 days.
## Mass in tube
A thin tube rotates at a constant angular velocity perpendicular to gravity. In this tube, a mass point moves friction-less.
Solving the problem for the position of the mass point makes use of moving reference systems, i.e. using the pseudo forces Coriolis and centrifugal force. Eulerforce is zero because of a constant angular speed.
After a lot of math, one arrives at the equation of motion ddot r - %omega^2 r = -g sin (%omega t + %varphi_0) , where r is the position of the mass from the center of rotation, ω the angular velocity, g the gravitational constant and φ0 the initial angle of the tube.
The term sin (%omega t + %varphi_0) is generated through solving the differential equation ddot x = -%omega^2 x (see file “Technical Topics”). The differential equation is in polar coordinates which are converted to x,y for the display with the help of the sine / cosine pair generated above.
Program: “TP1 06.18 Mass in Tube.AESL”
Scaling is done arbitrarily because we are investigation this problem only analytically.
6 situations have been investigated
1. Tube is initially horizontal
2. Tube is initially vertical
3. Tube is initially at an angle of 45° downwards
4. Under which condition does the mass point oscillate harmonically (φ(0)=0)?
   r0=0, r’(0)=v0=g/2ω
   The behavior is extremely sensitive to the parameters. A stable oscillation was not possible to set up.
5. Motion for v0+ω*r0=g/2ω (φ(0)=0)? v0 and r0 are chosen freely.
6. Motion for φ(0)=0, r(0)=0, r’(0)=0?

It is very instructive adjusting the various parameters and seeing the effect. Also one can see, that the behavior is near chaotic. The display shows various solutions at the same time due to fluctuations in the parameters generated by the tolerances of the electronics.
## Falling Mass
Calculate the deflection from the vertical caused by the Earth's rotation of a mass falling freely from rest from a height h.
Since the earth is a moving reference systems, the full equation of motion is
m ddot vec r' = vec F - m ddot vec R - m dot vec %omega times vec r' - 2 m vec %omega times vec v' - m vec %omega times ( vec %omega times vec r') .
On earth, ω ist constant, thus ω̇ = 0.
Furthermore, abs{vec r'} << R and ω² ≈ 0, which results in the equation with just the Coriolis force:
m ddot vec r' = vec F - 2 m vec %omega times vec v' .
Using vec F = - m g vec e_z', ~ vec %omega = %omega vec e_z results in the set of differential equations
alignl ddot x = -b dot z + a dot y newline alignl ddot y = - a dot x newline alignl ddot z = -g + a dot x newline alignc "with" newline alignl a:= 2 %omega sin %varphi, ~ b:= 2 %omega cos %varphi
with φ as the latitude of location (0-90°).
The script can be found in “TP1 07.19 Falling Mass.AESL”.
### Scaling
The rotation of earth (2π/24 h) is reflected in the constants a and b. Converting this to seconds results in a very small value (72,72*10-6). This value can be achieved by concatenating two coefficient potentiometers of which on is set to 0,01.
x and y are expected to be in cm to m whereas z is in the range of 100 m.
The solution is to measure z, ż and z˙˙ in a unit of 100 m and to remain with the other values in m. Here ż is needed to calculate x˙, so ż has to be multiplied by 100 to convert to m, which can be done by the coefficient b. It is very small so this multiplication comes very handy.
Also x˙ should be converted to 100 m by dividing a by 100. However, a is already tiny, so that we can approximate a by zero instead.

### Measurements
1. Where is the largest deflection?
  Adjusting a and b, which contain the latitude shows that the largest deflection is with sin φ = 0, i.e. cos φ = 1, i.e. φ = 0°, i.e. at the equator.
2. How large is the deflection at that location?
  Time to reach ground is measured to 6,585 ms (i.e. 6,585 s in the application), calculated is 6,386 s.
  At that time x has the value of 63 mV (i.e. 63 mm). Calculated is 62 mm. y is still on noise level thus negligible.
  At my home location with 51,7° latitude, the deflection is still at 41 mm.
# Notes
Useful links:
- Solving differential equations: https://www.wolframalpha.com
- Calculating derivatives: https://www.ableitungsrechner.net/