description Language for Analog Circuit Engines (LACE)
# Version History
‍2024-07-05	renamed to LACE; removed brackets for some operations; parameters are separated by space, comma or line break	Dietmar Hiller
2024-06-01	added operation output, division in isum	Dietmar Hiller
2024-05-29	First draft, still work in progress	Dietmar Hiller

License: CC BY-NC-SA 4.0 (https://creativecommons.org/licenses/by-nc-sa/4.0/ )
# Introduction
LACE (Language for Analog Computer Engines) is another scripting language for analog engines. In contrast to AESL, which is focused on connectivity of the engine, it is rather focused on function, user readability and simplicity. Thus realizing the connections requires more effort than with AESL.
# Basics
In the following descriptions, optional values are enclosed in [] brackets.
Parameters are separated by one or more spaces, comma or by a line break, where the following line(s) are indented (similar to Python). Example:
command input -> output parameter1 parameter2
is equivalent to
command input -> output
parameter1
parameter2
The second format is preferred to improve readability.
Variable names can be chosen relatively freely. Thus, same as with AESL it is recommended to use readable formulas such as “A+B”. Only the reserved words are not permitted.
Variables with the same name are connected on the wiring board.
Keywords and variables are case sensitive.
A comment starts with the character “#” and can be placed in a separate line or at the end of a command.
## Reserved Words
The following expressions may not be used for variables. They may not
… start with
- /
… contain
- <space>, <comma>
- :, #, =, ->
… be
- -1, +1
- 1, 10, 100
- 1*, 10*, 100*, 1000*
- capacitor
- coefficient
- compare
- GT0
- IC
- iintegrate
- invert
- isum
- limit
- loopback
- LT0
- multiply
- output
# OperationsCoefficients / Constants
There are two formats for coefficients:
coefficient(number): coefficient_name
The coefficient is referenced by coefficient_name.
This format is used to multiply a variable_name with a constant set by this coefficient.
coefficient(number): input -> coefficient_name
This is used to generate constants. input is “+1” or “-1” and thus the coefficient generates a positive or negative constant

number is the number identifier of the coefficient.
## Comparing
If variable_1 + variable_2 > 0, then variable_3 is available at variable_5, otherwise variable_4 is available.
compare variable_1 variable_2 -> variable_5
GT0: variable_3
LT0: variable_4
## Integration
Inverted integration of the sum of weighted input values over time.
iintegrate [weight*: ]variable-1 [[,] …] -> variable-n
[IC: variable-IC]
[limit: GT0]
[SLOW]

weight can be 1*:, 10*:, 100*: etc. The value of the variable is multiplied by this weight. weight can be omitted for 1*:.
IC is the initial condition. It has the same sign as the input. If omitted 0 is used.
limit limits the output variable-n:
- GT0: limits to values > 0.
  - realized by variable-n -> cat:diode -> SJ of integrator
  - There is a small slag, thus the output takes a tiny negative value. As soon as the cathode of the diode gets negative, the input of the integrator is short-circuited to the output and inhibits further integration.
SLOW reduces the speed of the integration. All integrators have to use the same speed.
  - realized by output -> SLOW
## Inverting
Invert variable_name1 giving variable_name2.
invert variable_name1 -> variable_name2
## Multiplication
### of 2 variables
Multiply variable_x by variable_y.
multiply variable_x[,] variable_y -> variable_name
### of a variable with a constant
variable_1 * coefficient_name -> variable_2

Multiplies variable_1 with coefficient_name giving variable_2. The value of coefficient_name is in the range of [0 .. 1].
It is realized by connecting variable_1 to the corresponding coefficient.
## Summing
Inverted sum of the weighted input values.
isum [weight*: ]variable-1 [[,] …] -> variable-n
[/divisor]

weight can be 1*:, 10*: etc. The value of the variable is multiplied by this weight. weight can be omitted for 1*.
divisor can be 2, 3, …
/2 is realized by: variable-n -> SUMMER
/3 is realized by: variable-n, variable-n -> SUMMER
...
## Open Amplifier
The open amplifier can be used to generate further functionality.
openamp [weight*: ]variable-1 [[,] …] -> output
loopback: capacitor(capacitance)

The open amplifier is generated by connecting in a SUMMER FB to GND.
weight works the same as in the SUMMER.
loppback: defines the loopback from output to SJ. It can be
  - capacitor(capacitance): to generate the functionality of iintegrate.
  - realization: output -> capacitor.capacitance -> SJ
## Output
Describes varibles which are connected to the output of the engine.
output(identifier): variable-name

identifier can be e.g. x, y, z, u.