Analog Engine
Example Applications
This document includes examples of applications realized with an analog engine. The scripting language used is described in the document “Analog Engine Scripting Language”.
Author: Dietmar Hiller
License: CC BY-NC-SA 4.0 (https://creativecommons.org/licenses/by-nc-sa/4.0/ )
# Version History
‍2024-01-31	corrected 10¹ is da (deca) / License CC BY-NC-SA / Application: 2 raindrops	Dietmar Hiller
‍2024-01-24	Some general details / Mass at the apex on a sphere	Dietmar Hiller
‍2024-01-16	Added: Mass with charge in e/m field	Dietmar Hiller
2024-01-08	Separated Helper Functions and Scaling to “Technical Topics” / Moved code to separate files AESL / Analytical solution of the damped harmonic oscillator / Scaling amplitude and time	Dietmar Hiller
2023-10-06	Adapt to updated syntax: OUT.U use of ALIAS / corrected usage of operation time: OP-TIME instead of SPEED	Dietmar Hiller
2023-10-04	Added damped harmonic oscillator	Dietmar Hiller
2023-09-24	First draft	Dietmar Hiller

# Example Applications
## Radioactive Decay
N’ = -lambda * N
+1 -> InitialValue -> N0
N’, IC:N0 -> Integrator.1 -> -N
-N -> Decay -> -lambda*N=N’
-N -> Inverter.1 -> N

Note that the integrator is inverting the sign and that the initial condition has the same sign as the input.
Full code see “Radioactive Decay.AESL”
## Damped Harmonic Oscillator
The equation of motion for a viscously damped simple harmonic oscillator is m ddot{y} + D dot{y} + S y = 0 , with m the mass, D the damping with speed and S the spring constant.
Rewritten to y’’=-1/m * (Dy’+Sy).
An initial condition is required; we put the deflection to y0 and the speed to y0’.
Full code see “Damped Harmonic Oscillator.AESL”
### Analytical Solution
[https://brilliant.org/wiki/damped-harmonic-oscillators/ ]
Solutions of the viscously damped simple harmonic oscillator should be oscillations within some form of damping envelope. Ansatz is an exponential damping envelope of an oscillation:
y(t) = Ae^{-g t} e^{iat} = Ae^{t (ai-g)} = Ae^{rt}
where A is some constant and (r = ai-g) will be found. g and a are place holders to show the damping (g) and oscillation (a). Plugging this ansatz into the equation of motion yields:
(mr^2 + D r + S)Ae^{rt} = 0 newline drarrow r^2 + frac{D}{m} r + frac{S}{m} = 0
which is a quadratic equation in r with solutions:
r = - {frac{D}{2m}} +-i cdot sqrt{ {frac{S}{m}} - frac{D^2}{4m^2} }
Note that there are two roots r to the quadratic corresponding to the two general solutions:
y(t) = a_1 e^{-frac{D}{2m} t} e^{ i sqrt{{frac{S}{m}} - frac{D^2}{4m^2} }t} + a_2 e^{-frac{D}{2m} t} e^{ -i sqrt{{frac{S}{m}} - frac{D^2}{4m^2} }t}.
These solutions in general describe oscillation at frequency %omega = sqrt{{frac{S}{m}} - frac{D^2}{4m^2} } within a decay envelope of time-dependent amplitude %alpha(t) = e^{-frac{D}{2m} t} .
Note, the frequency of the oscillations is only depending on the spring constant, damping and mass, whereas the damping also depends on the mass.
For the undamped case (D=0) this gives
alignl y(t) = a_1 e^{i %omega t} + a_2 e^{-i %omega t} newline alignl y(t) = a_1 cdot (cos (%omega t) + i sin (%omega t)) + a_2 cdot (cos (%omega t) - i sin (%omega t)) newline alignl y(t) = (a_1 + a_2) cdot cos(%omega t) + i (a_1 - a_2) sin (%omega t) newline alignc a_1 + a_2 = A newline alignc i(a_1 - a_2) = B newline alignl y(t) = A cos(%omega t) + B sin(%omega t) newline alignc y(t=0) = y_0 = A newline alignc dot y(t=0) = v_0 = B %omega newline alignl y(t) = y_0 cos(%omega t) + frac{v_0}{%omega} sin(%omega t)
This can also be written as
alignl y(t)=b cdot cos(%omega t - %varphi) newline alignc "because of" newline alignc y(t)=b cdot (cos(%omega t) cdot cos (%varphi) + sin(%omega t) cdot sin(%varphi) ) newline alignc y(t)=b cdot cos(%varphi) cdot cos(%omega t) + b cdot sin(%varphi) cdot sin(%omega t) newline alignc "with" newline alignc x_0 = b cdot cos(%varphi) newline alignc frac{v_0}{%omega} = b cdot sin(%varphi)

### Scaling
As an example, we may use the following data for the damped harmonic oscillator:
Initial Position	y0	1,5 m
Initial Speed	y0’	-0,15 m/s
Spring Force	S	2,5 N/m	kg/s²
Damping	D	0,3 N/(m/s)	kg/s
Mass	m	0,06 kg
	1/m	16,667 kg-1

Critical values are initial position (1,5 m) and 1/m (16,667 kg-1). Spring force could be coped with by using a gain 10 input.
Please see the table below while following the description of the following steps.
First we take care of y0. We replace the length measured in meter with 10¹ meter, thus we make use of deca-meter. y0 and y0’ have to be adapted. See columns “deca-m” below. Spring Force and Damping remain unchanged because in base units the length gets canceled out.
Next issue is that 1/m is well above 1. We are representing the weight by 10-2 kg, so 10¹ grams (deca-g). See columns “deca-g”. This also influences spring force and damping, which now exceed our target range.
Now, the second is replaced by 10-1 (deci-s) seconds resulting in the columns “deci-s”. Note that this also performs time-scaling, so that one time-unit of the analog engine now corresponds to one deci-second instead of one second before.
After the last scaling we have the issue that y0’ is very close to zero. There are more advanced scaling techniques which manage to optimize the value range of each operational amplifier. For instance the initial speed is converted to a value very close to zero, which is not the optimal.
The fully scaled program can be found at “Damped Harmonic Oscillator scaled.AESL”. Note that the gain 10 inputs are used for SUMMER.2 in order to achieve damping and spring constant values:

Obtained damped oscillation with parameters above
Adapted parameters: D=1,69, y0'=-0,187; calculated T=9,97 ms
## Mass with charge in em field
A mass m with charge q>0 is located in a static electro-magnetic field [0,0,E], [0,-B,0]. Calculate the trajectory of the mass. The Lorentz-force is causing the motion of the mass.
alignl m ddot vec r = q (vec E + vec v times vec B) newline alignl m left [ stack{ddot x # ddot y # ddot z} right ] = q left ( left [stack{0 # 0 # E} right ] + left[ stack{v_x # v_y # v_z} right] times left[ stack{0 # -B # 0} right] right ) = ~ q left ( left [stack{0 # 0 # E} right ] + left[ stack{v_z B # 0 # -v_x B} right ] right) = ~ q left ( left [stack{v_z B # 0 # E -v_x B} right ] right) .
Which results in the two differential equations
alignl ddot x = {q} over {m} dot z B newline alignl ddot z = {q} over {m} (E -dot x B) = q over m E - %omega dot x newline with %omega := q over m B , ~ a := {m E} over {q B^2} = {q E} over {%omega^2 m} newline alignl ddot x = %omega dot z newline alignl ddot z = a %omega^2 - %omega dot x newline
with the solutions
alignl x(t) = a (%omega t - sin (%omega t)) ~ rightarrow dot x(t) = a %omega (1- cos (%omega t)) ~ rightarrow ddot x(t) = a %omega^2 sin (%omega t) newline newline alignl z(t) = -a cos(%omega t) + z_0 newline with z(0)=0 newline alignl z(t) = a (1- cos(%omega t)) ~ rightarrow dot z(t) = a %omega sin (%omega t) ~ rightarrow ddot z(t) = a %omega^2 cos (%omega t) newline
This is the trajectory of a cycloid.
The AESL-program can be found in file “Charge in em field.AESL”.
It is interesting and easy to play with initial speed conditions.
Trajectory of a charge mass in an em field (omega=0,92; a*omega²=0,05; OP-time=0,21ms)	Added initial speed in x and z-direction

## Mass at the apex on a sphere
A mass m rests at the apex on a fixed sphere with radius a. With a slight displacement, it slides down the sphere without friction.
We are making use of Lagrange equations of the 1st kind.
### Equations of motion
alignl m vec ddot r = m vec g + 2 %lambda(x,y) newline alignc "so" newline alignl m ddot x = 2 %lambda x newline alignl m ddot y = 2 %lambda y - m g newline alignc "with the motion forced to the sphere" newline %varphi = x^2 + y^2 - a^2 = 0 ~->~ ddot %varphi = {dot x}^2 + x ddot x + {dot y}^2 + y ddot y = 0
### Calculating λ
Insertion of the equations of motion
alignl {dot x}^2 + x {2 %lambda x} over m + {dot y}^2 + y left( {2 %lambda y - m g} over m right) = 0 newline alignl {dot x}^2 + {dot y}^2 + {2 %lambda} over m left( x^2 + y^2 right)- g y = 0 newline alignl v^2 + {2 %lambda} over m a^2 - g y = 0 newline alignl %lambda = m over {2 a^2} left( g y - v^2 right)
v² is determined by the law of conservation of energy
E = 1 over 2 m v^2 + m g y = m g a newline v^2 = 2 g (a - y) newline alignl %lambda = m over {2 a^2} left( g y - left( 2 g (a - y) right) right) ~=~ {m g} over {2 a^2} left( 3y - 2a right)
### Final equations of motion
alignl m ddot x = 2 left( {m g} over {2 a^2} left( 3y - 2a right) right) x newline alignl m ddot y = 2 left( {m g} over {2 a^2} left( 3y - 2a right) right) y - m g newline alignl ddot x = {3 g} over a^2 x y - {2 g} over a x newline alignl ddot y = {3 g} over a^2 y^2 - {2 g} over a y - g
### Program
Scaling is done simply by using da-m (10¹ m) instead of meter in order to have g=0,981 da-m/s². Thus also a, x, y are measured in da-m. The constants are thus:
‍Const	Coefficient	Example	Unit
a		1,000	da-m
g	C5	0,981	da-m / s²
3 g / a²	C1 (for x*y), C2 (for y^2)	2,943	1 / (da-m * s²)
2 g / a	C3 (for x), C4 (for y)	1,962	1 / s²
x0	C6 (=root(a² – y0²))	0,957	da-m
y0	C7	0,290	da-m

The display of the oscilloscope is extremely sensitive to these parameters and the tolerances of the potentiometers. E.g. C6=1 had to be set to get a good result.
The full program can be found in file “4.10 MassOnSphere.AESL”
## Two raindrops
Two raindrops of same size and altitude are falling towards the earth. How long does it take until the touch due to the gravitational force between them.
As this is a multi-mode problem, we make use of the reduced mass (1/µ = 1/m1 + 1/m2). This gives the differential equation
µ ddot s = - {%gamma m_1 m_2} over s^2
With m1=m2: µ=m/2, with m=m1=m2 thus
m over 2 ddot s = - {%gamma m^2} over s^2 ~ -> ~ ddot s = - 2 {%gamma m} over s^2 .
The fact that the mass is divided by 2 can be understood by the fact that both raindrops are attracting each other, thus reducing inertia.
### Scaling
Looking at the values for this calculation, the need for scaling is evident:
- Radius of the raindrops: r=1mm
- Initial distance: 2 mm
- Constant of gravity: γ=6,672*10-11 m³/(kg s²)
- Density of water: ρ=1 kg / dm³
- Mass: m=4π/3*ρ*r³=4,189*10-6 kg

First, cm are used for the lengths, which also puts the size of the drops to a usable value. However, the constant of gravity still remains too small. Next, time is measured in 10⁴ s.

Which gives the settings:
- 2r	0,200 cm
- s0	0,400 cm
- 2gamma*m	0,056 cm³/(10^4 s)²
Timescale is: 1 Timebase = 10⁴ s
### Measurement
The time until the two drops touch is measured to 975 µs.
Timebase of THAT is 1 ms, thus the measured time is
10⁴ s * 0,975 ms / 1 ms = 9750 s = 2,71 h, which corresponds to the calculated value.
AESL-Script: “4.11 TwoRaindrops.AESL”
# Notes
Useful links:
- Solve differential equations: https://www.wolframalpha.com
- Calculate derivatives: https://www.ableitungsrechner.net/