CoBolD
Control-BoarD

The purpose of this project is to develop a stand-alone board with touch-screen to control digital and analog interfaces. Basis shall be a hardware oriented set-up with plug-ins for custom applications.
# Hardware
## Board
- Olimex OLinuXino A20-OLinuXino-LIME2-e16Gs16M [1][2][3]
  - 16 GB eMMC (later-on for OS)
  - 16 MB SPI Flash (SPI tests)
  - Touch Screen requires resistor matrix RM2 for digital interface, has to be specified when ordered [4]
  - PCB dimensions: (84 x 60)mm
  - Cost: 53,00 € + VAT + Shipment
## Adapter
- Adapter to exhibit GPIO and serial ports
- Olimex LIME2-SHIELD [5]
  - 40 port digital IO GPIO connector with 0.1" step
  - 2x UEXT for analog communication
  - 1x CAN bus
  - Audio in / out
  - extra microSD-Card
## Power Supply
- Olimex SY1005E [6]
  - Output: regulated 5V 2A
  - Cost: 6,95 € + VAT + Shipment
## Housing
- Olimex BOX-LIME-BLACK [7]
  - Dimensions: 100 x 70 x 25 mm
  - Cost: 8,00 € + VAT + Shipment
## Touch Screen
- Olimex LCD-OLinuXino-5CTS [8]
  - capacitive touch screen (multi-touch)
  - Screen: 5“, 800×480 px
  - Outline dimensions 120.7(H) X 76.3(V) X 3.0(D) mm
  - needs: CABLE-40-40-10CM
    - 0.05'' step cable for connecting a display, 40-pins, 10 cm long
    - 3,00 €
  - Cost: 40,00 € + VAT + Shipment
## USB to SERIAL CABLE
- Olimex USB-SERIAL-F [9]
  - for debugging on UART0 // BB-CH340T USB-serial converter
  - Cost: 5,95 € + VAT + Shipment
## WLAN
- USB-WLAN adapter:
  - MOD-WIFI-R5370: 9,00 € + VAT + Shipment
# Operating System
## Image
1. Follow instruction from [2] > Software > Olimex Linux Guide [10]
2. Download from https://images.olimex.com/release/a20/
3. Extract the file to img
4. Check md5sum:
   md5sum -c A20-OLinuXino-bullseye-base-20211223-102355.img.md5
5. Put (at least 4GB) microSD card in your card reader [3]
6. Identify dev/sdX
7. Transfer image to microSD:
  1. either via Nautilus, right-click
  2. or dd if=a20_Lime2_debian_second_release.img of=/dev/sdX
## Control Computer
1. Install putty
  1. plug in USB to serial adapter
  2. identify serial port name:
    1. ls -l /dev/serial/by-id
    2. name is e.g. ttyUSB0
    3. note: owner is root, must be called with sudo
## Hardware for Installation
1. Insert microSD-Card
2. Connect Touch Screen with Cable
3. Connect Serial to USB converter:
  1. GREEN RX line of the cable to TX line of the target board (left)
  2. RED TX line of the cable to the RX line of the target board (mid)
  3. BLUE wire to the target's GND line (right)
4. Connect LAN cable to router
5. Connect and power on HDMI TV
6. Connect USB hub with keyboard and mouse
## Installation of Operating System
1. Connect Serial to USB convert to control computer
2. Start putty as sudo
      - connection type: serial
      - serial line: /dev/ttyUSB0
      - settings: 115200 baud, 8-N-1
Power on the board
      - Installation starts
      - XFCE is automatically started on HDMI screen
1. Log in: The default username is root and the default password is olimex.
2. Restart
3. Upgrade system (aptitude already pre-installed):
  1. apt update
  2. apt upgrade
4. Set locales:
  1. for GUI: sudo dpkg-reconfigure locales
  2. for keyboard: temporarily: setxkbmap -layout de
     https://wiki.archlinux.org/title/Xorg/Keyboard_configuration#Using_localectl :
     localectl --no-convert set-x11-keymap de
# Additional Hardware
WLAN
  1. Plug in WLAN adapter
  2. in XFCE “Settings > Advanced Network Configuration”
    1. add LAN and WLAN connection
    2. note IP-Address
  3. detach LAN cable
1. SSH access
  1. disconnect putty
  2. ssh olimex@<local address>
2. Enable 5” screen
  1. run script olinuxino-display
  2. detach HDMI screen cable
  3. restart
# Ports
Brainstorming:
## GPIO
see [11]
Configuration: input | output
- pull-up: pull-up | pull-down
- high | low
## I2C
- Status:
  - init | not yet init
  - open | close
## SPI
Status: open | closed
# Software
Concept: The interface shall be controlled via a small (5”) touch screen. Basis will be direct access to the I/O ports (digital, analog, CAN etc.) with simple setting and reading of values.
On top of this basis, layers can be placed. A layer represents an application with a set of I/Os. In these layers the I/Os will be controlled in their function, e.g. closing a valve or reading a temperature. Layers shall be easy to develop and to add, e.g. as plug-ins, without tempering with the basic software.
Layers can be stacked, e.g. a layer like “temperature controlling” can make use of layers below like “thermometer” and “valve control”.
The layers can be selected with a layer button (which opens a selection screen).
Another button shall provide access to application specific data, such as “about”.
These two buttons shall be omnipresent, e.g. in the title bar. The rest of the screen shall be freely adjustable in the layers.
## Development Environment
- GUI development via GTK: GLADE
  - GTK tutorial: https://python-gtk-3-tutorial.readthedocs.io/en/latest/
  - Python API reference: https://lazka.github.io/pgi-docs/
- IDE: GeAny